## Slide 1: Module 5: Train-the-Trainer
Notes: Complete Narration: “This is North American Fatigue Management Program Module 5, Train-the-Trainer. In this module you will learn how to conduct classroom training and assist web-based training of Module 3, Driver Education, and Module 4, Family Education.”

## Slide 2: Module 5 Overview
Introduction
Train-the-Trainer Overview
FMP Training Overview
Trainer Requirements & Responsibilities
Web-Based Training
Effective Instruction
Driver Education Training, Part 1
Driver Education Training, Part 2
Family Education Training & Behavior Change
Family Education Training
Facilitating Behavior Change
Review & Conclusion
Notes: Complete Narration: “Here is an overview of this module. This introduction will be followed by a train-the-trainer overview. This will include the overall FMP training program, trainer requirements and responsibilities, a discussion of web-based training, and tips for effective instruction. The next two lessons will review the driver education module, both in regard to its content and methods of instruction. After that, the next lesson will address family education training, and will also discuss the process of behavior change, and your role as an agent of positive change. This module will conclude with a review and 30-item exam.”

## Slide 3: Trainer Functions in the FMP
Coordinate and teach Module 3 in a classroom setting
Coordinate and teach Module 4 at carrier family events
Facilitate driver and family web-based learning
Develop subject matter expertise
Possible additional responsibilities:
  Maintain carrier FMP records
  Take, and possibly teach, other FMP modules
  Conduct webinars
Notes: Complete Narration: “FMP trainers perform various functions. You will coordinate and teach Module 3 (Driver Education) in classroom settings, and Module 4 (Family Education) at carrier family events. You will facilitate driver and family web-based learning. You will develop fatigue subject matter expertise so you can become a carrier expert and mentor. You may have other responsibilities such as maintaining carrier FMP records. You may take, and possibly teach, other FMP modules. Finally, many large and progressive carriers have the capability to conduct webinars. A webinar has a real-time instructor like classroom training, but students access the instruction from remote locations via computer and/or telephone.
___________________
Additional instructor note: As part of its NAFMP planning, your company should identify and specify trainer functions and responsibilities. This would include those listed above as well as specific additional responsibilities.

## Slide 4: Module 5 Train-the-Trainer Learning Goals (1 of 3)
Knowledge:
  Know the structure and procedures of the FMP & its training program
  Understand the principles and methods of effective teaching
  Know the major facts and principles of driver fatigue, alertness, sleep, & wellness in sufficient detail to be able to teach them
Notes: Complete Narration: “Your learning goals for this module include new knowledge, skills, and attitudes. Your knowledge goals will be to:
  Know the structure and procedures of the FMP and its training program.
  Understand the principles and methods of effective teaching, and
  Know the major facts and principles of driver fatigue, alertness, sleep, and wellness in sufficient detail to be able to teach them.”
__________________
Additional instructor note: Specific Knowledge, Skill, and Attitude (KSA) learning objectives are provided for each module section. Successful NAFMP trainers will be those who are strong in all three areas: knowledge of both driver fatigue and training principles, skill in conducting classroom training and otherwise assisting learning, and positive attitudes about fatigue management (i.e., health- and safety-related behaviors).

## Slide 5: Module 5 Train-the-Trainer Learning Goals (2 of 3)
Skills:
  Classroom teaching
  Facilitate web-based learning
  Serve as effective role model and behavior change agent
Notes: Complete Narration: “You will acquire skills for classroom teaching, facilitating web-based learning, and serving as effective role model and behavior change agent.”

## Slide 6: Module 5 Train-the-Trainer Learning Goals (3 of 3)
Attitudes:
  Value sleep, alertness, and wellness as major factors in driver performance, safety, and happiness
  Commitment to train and manage drivers in ways supporting health and alertness
Notes: Complete Narration: “Attitudes are the feelings we have toward things. They may be positive or negative. Having a positive attitude toward fatigue management is probably just as important as developing knowledge of the subject. At the completion of this module you should value sleep, alertness, and wellness as major factors in driver performance, safety, and happiness. In addition, you should accept a commitment to train and manage drivers in ways supporting health and alertness.”

## Slide 7: Train-the-Trainer Overview
Notes: Complete Narration: “Our first main lesson will include an overview of the FMP training program, trainer requirements and responsibilities, a discussion of the web-based training structure and features, and tips for effective instruction.”

## Slide 8: FMP Training Overview
Topics:
Training program organization
Module 3 overview
Module 4 overview
Instructional methods & procedures
  Classroom teaching
  Facilitating web-based learning
Notes: Complete Narration: “Let’s overview the FMP training program. This will include its organization, an overview of Module 3, and an overview of Module 4. We’ll also discuss instructional methods and procedures for classroom teaching and for facilitating web-based learning.”
____________
Additional instructor note:
Section learning objectives:
(K) Identify all FMP modules.
(K) Identify key characteristics of Modules 3 and 4 (e.g., target audience, time required)
(K) Identify instructional methods and procedures for Modules 3 and 4.

## Slide 9: Ten FMP Instructional Modules
Module | Title | Target Audience | Estimated Duration
1 | FMP Introduction and Overview | Carrier Executives and Managers | 45 minutes
2 | Safety Culture and Management Practices | Carrier Executives and Managers | 1.5 hours
3 | Driver Education | Drivers | 3 hours
4 | Driver Family Education | Drivers’ Spouses and Family | 45 minutes
5 | Train-the-Trainer for Driver Education and Family Forum | Trainers | 3.5 hours
6 | Shippers and Receivers | Shippers and Receivers | 30 minutes
7 | Motor Carrier Sleep Disorders Management | Carrier Executives and Managers | 1.5 hours
8 | Driver Sleep Disorders Management | Drivers | 1.25 hours
9 | Driver Scheduling and Tools | Dispatchers and Managers * | 1 hour
10 | Fatigue Monitoring and Management Technologies | Carrier Executives and Managers | 1 hour
Notes: Complete Narration: “The ten FMP instructional modules are shown here. You are probably already familiar with several of these. The two you will be qualified to teach, Driver Education and Family Education, are highlighted.”

## Slide 10: Module 3 Overview
Introduction Introduction to Module Sleep, Alertness, Wellness, & Performance Lesson 1: Characteristics of Fatigue & Fatigue Crashes What is Fatigue? Fatigue Characteristics Fatigue-Related Crashes | Lesson 2: Sleep & Other Factors Affecting Alertness What is Sleep? Factors Affecting Alertness & Performance Individual Differences in Fatigue Susceptibility Lesson 3: Health, Wellness, Drugs, & Medications Health & Wellness Drugs & Medications | Lesson 4: Alertness & CMV Driving Improving Sleep & Alertness Scheduling & HOS Team Driving Conclusion Review Module Exam
Notes: Complete Narration: “Here we see the lessons and topics of Module 3, Driver Education. It consists of an introduction, four main lessons, and a conclusion. Prior completion of Module 3 is a prerequisite to taking this train-the-trainer module.”

## Slide 11: Module 4 (Family Education)
Introduction
Fatigue Basics
Alertness, Sleep, Wellness, & Performance
What is Fatigue?
Fatigue Characteristics
Fatigue-Related Crashes
Physiology of Sleep & Alertness
What is Sleep?
Factors Affecting Alertness & Fatigue
Sleep Disorders
Health & Alertness
Health & Wellness
Drugs & Medications
Improving Sleep & Alertness
Conclusion
Notes: Complete Narration: “Here are the lessons and topics of Module 4, Family Education. You should have already completed this module also. Module 4 topics are a subset of those in Module 3. Included are topics most relevant to home life and of concern to drivers’ families. Module 4 attempts to reach out to families to increase their appreciation of driver sleep needs. It enlists their support for more healthful behaviors. The same behaviors that benefit drivers are likely to benefit their family members as well.”

## Slide 12: Instructional Methods
PowerPoint
  Classroom
  Traditional instructor role
  Lead group discussions
  Administer quizzes & exams
Web-based
  Individual students online
  Students can be alone or in group setting
  “Instructor” is facilitator, coach, & troubleshooter
Notes: Complete narration: “There are two primary FMP instructional methods. PowerPoint slides are designed for classroom use and a traditional instructor role. As part of this you will lead group discussions and administer quizzes and exams. The web-based instruction is taken by individual students online. They may be working alone or in group settings with multiple computers. Here, the instructor is a facilitator, coach, and troubleshooter. Later, we will briefly discuss a third instructional method, webinars, which combines some features of both classroom and web-based instruction.”
___________
Additional instructor note: Make sure that trainees do not confuse web-based training with webinars. They are two distinct modes of instruction. From the training perspectives, webinars are more like classroom training than like web-based training.

## Slide 13: Trainer Requirements & Responsibilities
Topics:
Requirements
  General qualifications & skills
  Specific requirements
Responsibilities
Notes: Complete Narration: “This section covers trainer requirements and responsibilities. To be effective as a trainer, you need a number of general qualifications and skills. In addition, there are specific requirements relating to the FMP modules. Once you are qualified and ready to go, you will have several areas of responsibility.”
____________
Additional instructor note:
Section learning objectives:
(K) Recognize general trainer qualifications and skills necessary for effectiveness.
(K) Recognize specific NAFMP trainer requirements.
(K) Recognize trainer roles and responsibilities for both group and individual web-based training.
Accept need to become fatigue subject matter expert.
(A) Accept need to develop and actively employ instructor skills.

## Slide 14: Trainer Requirements: General Qualifications & Skills (1 of 2)
Must have:
Job knowledge & experience
Training experience
Model behavior
Ability to relate well with people
Enthusiasm
Company loyalty
Ethics
Notes: Complete Narration: “In almost any area of occupational training, trainers must have certain qualifications and skills. These include job knowledge and experience, training experience, model behavior, the ability to relate well with people, enthusiasm, company loyalty, and ethics.”
__________
Additional instructor note: In addition to those shown, other needed qualities are leadership skills, willingness to work irregular hours, ability to emphasize with students problems, and flexibility. Principal source: Birnbrauer and Tyson, 1985.

## Slide 15: Trainer Requirements: General Qualifications & Skills (2 of 2)
Must have or develop:
Presentation skills
Computer skills
Understanding of adult learning & motivation
Ability to create learning environment
Listening and positive reinforcement skills
Knowledge of company policies
Understanding of behavior change
Notes: Complete Narration: “In addition, you must have, or be able to develop, presentation skills, computer skills, an understanding of adult learning and motivation, an ability to create a learning environment, listening and positive reinforcement skills, knowledge of company policies (both operational and personnel-related), and an understanding of behavior change. Remember, the ultimate goal is to change driver behavior in positive ways.”
______________________
Additional instructor note:
Principal source: Birnbrauer and Tyson, 1985.

## Slide 16: Specific Trainer Requirements
Prior successful completion these modules with an 80% or higher average exam score:
  Module 1: FMP Introduction & Overview
  Module 3: Driver Education
  Module 4: Family Education
Prior successful completion of at least one FMP training module (preferably Module 3) in the web-based mode
Successful completion of this module with an 80% or higher exam score
Notes: Complete Narration: “There are also specific trainer requirements, including prerequisites. You must have successfully completed Modules 1, 3, and 4 with exam scores of 80% or higher. You must have successfully completed one training module (preferably Module 3) in the web-based mode so you are familiar with that process. Finally, you must complete this module with an 80% or higher exam score.”

## Slide 17: Trainer Responsibilities
Gain additional knowledge on driver fatigue
Conduct classroom training of Modules 3 and 4
Oversee and facilitate web-based learning
Keep FMP training records
Notes: Complete Narration: “As a trainer, you will have these responsibilities. First, you must continue to gain additional knowledge on driver fatigue and related topics. Your principal activities will be to conduct classroom training of Modules 3 and 4, and to oversee and facilitate web-based learning. Also, you will likely be responsible for keeping records of FMP training for your carrier.”
____________
Additional instructor note: Possible check on learning: Q: The exam for this module will have 30 questions. How many must you answer correctly to pass? A: 24 of 30, or 80%.

## Slide 18: Web-Based Training
Topics:
Advantages
FMP website & Learning Management System (LMS)
Supervising & assisting trainees
Testing & record-keeping
Notes: Complete Narration: “This section covers the web-based FMP training. The web-based training has the same content as the classroom training, but the mode of delivery is quite different. We’ll discuss its advantages, the FMP website, Learning Management Systems, supervising and assisting trainees, and testing and record-keeping.”
___________
Additional instructor note: Web-based training is best learned through doing it, as opposed to talking about it. This section is relatively short and is intended to establish NAFMP trainers’ responsibilities relating to web-based training. They should be thoroughly experienced and practiced in the web-based modules before actually assisting students using them.
Section learning objectives:
(K) Identify advantages and applications of web-based training.
(K) Identify FMP website characteristics and use in training.
(K) Recognize specific trainer tasks and responsibilities.
(S) Be able to effectively coordinate and facilitate NAFMP web-based training at the company level.

## Slide 19: Advantages of Web-Based Training
Easier access
Convenient and flexible for learners
Interactive & engaging
Reduced training time
Standardized
Economies of scale
Easier tracking of trainee performance
Easier organizational record-keeping
Notes: Complete Narration: “Web-based training has a number of advantages over conventional classroom instruction. Training access is easier, and with greatly reduced travel time and expenses. Web-based training is convenient and flexible for learners. Good web-based training is interactive and engaging, and usually results in reduced training time because each learner can move ahead at his own pace. Web-based training provides both standardized instruction and economies of scale. It also provides easier tracking of trainee performance and easier record-keeping for the organization.”
______________
Additional instructor note: Source: Brock et al., 2011. Web-based training can be applied to almost every topic area, in particular those with a lot of terms and concepts like fatigue training. WBT results in superior learning than classroom training for many topic areas, though not all. One area where web-based training doesn’t work well is procedural training where trainees must learn by actually performing the task (e.g., auto repair procedures).

## Slide 20: FMP Website & Learning Management Systems
Website:
  Central location for NAFMP information, materials, and services
  Users may access web-based modules
Carriers with computer-based training Learning Management Systems (LMSs)
  May download modules in HTML format
  Carrier LMS would track student activities:
    Entrance to module
    Progress
    Exam scores
    Completion status
Notes: Complete Narration: “The NAFMP website is the central location for information, materials, and services. Users may access the web-based training modules from the website. If a carrier has its own Learning Management System (or LMS), it may download the modules in HTML format, and use its LMS to manage the training. LMSs track student activities, including entrance to a module, progress, exam scores, and module completion status.”
_____________
Additional instructor note: If your carrier has its own LMS to support the NAFMP training, or has otherwise acquired access to an LMS, you should be thoroughly familiar with it, and provide trainees with specific additional information on it.

## Slide 21: Supervising & Assisting Trainees
Identify drivers (& others) to be trained
Orient students to module content & requirements
Ensure students have adequate computer access & log-on info
Assist students as needed (in-person or remotely)
Answer questions
Monitor progress
Troubleshoot any technical or learning problems
Notes: Complete Narration: “Your role will be to supervise and assist trainees taking the web-based training. You will identify drivers (and others) to be trained, orient students to module content and requirements, and ensure that students have adequate computer access and log-on information. You will assist students, whether that assistance is provided in-person or remotely via computer or telephone. You will answer questions, monitor progress, and troubleshoot any technical or learning problems.”
___________________
Additional instructor note: A trainer’s effectiveness in providing the above assistance is likely to be strongly correlated with his/her own experience and facility in using the web-based modules.

## Slide 22: Testing & Record-Keeping
If a carrier has a Learning Management System (LMS), it will track online exam scores and student completion of modules
Lesson quiz scores are not recorded
Exam scores are recorded
Three attempts at each exam are permitted; only highest score is retained.
Notes: Complete Narration: “Testing and record-keeping are part of the training process. If a carrier has an LMS, it will track online exam scores and student completion of modules. Lesson quiz scores are not recorded, but exam scores are recorded. Three attempts for each exam are permitted, but only the highest score is retained in the system.”
______________________
Additional instructor Note. Check on learning: Q: We listed 8 different advantages of web-based training. Can you remember any four of them? A: Any 4 of these 8: Improved learning, easier access, convenient and flexible, standardized, faster, economies of scale, easier tracking of trainee performance data, easier record-keeping.”

## Slide 23: Effective Instruction
Topics:
What is learning?
Characteristics of adult learners
Effective instructors
Learning principles incorporated into FMP training
Giving & receiving feedback
Creating a positive classroom experience
Webinars
Incorporating company examples
Maintaining standards & accountability
Notes: Complete Narration: “Our next topic is effective instruction. Topics include “What is learning?,” characteristics of adult learners, effective instructors, learning principles incorporated into the FMP training, giving and receiving feedback, creating a positive classroom experience, incorporating company examples into the training, and maintaining standards and accountability.”
____________________
Additional instructor note: This is a fairly long section which covers the principles and practices of effective instruction.
Section learning objectives:
(K) Recognize three outcomes of learning [“knowledges,” skills, and attitudes].
(K) Recognize ultimate fatigue management learning goal [behavior change].
(K) Identify key characteristics of adult learners.
(K) Identify key characteristics of effective trainers.
(K) Recognize key learning/training principles embedded in the FMP training.
(K) Recognize the feedback principle.
(S) Be able to provide frequent and positive feedback to students in the classroom.
(K, S) Identify ways to create and sustain a positive and engaging classroom environment, and be able to employ them.
(K,S) Identify techniques for leading group discussions and stimulating interactivity, and be able to employ them.
(K) Recognize value of interjecting company examples, policies, and other supplemental material into training.
(S) Be able to apply principles for effective learning in the classroom.
(A) Accept and value role as FMP trainer, role model, and company training coordinator.
(S,A) Through classroom practices, set a high standard for instructional effectiveness and student performance. Value these high standards as essential for successful instruction.

## Slide 24: What is Learning?
Learning is the acquisition of new:
Knowledge
Skills
Attitudes
In fatigue management, the ultimate goal is behavior change
Notes: Complete Narration: “Learning is the acquisition of new knowledge, skills, and attitudes. These are often called KSAs. As people become more educated, they make more informed choices about their behavior. In fatigue management, the ultimate goal is behavior change.”
_____________
Additional instructor note: Overall, most of the NAFMP training is directed toward knowledge goals. For Modules 3 and 4 especially, the general instructional strategy might be summarized as: Increase knowledge  Change attitudes  Change behavior  Improve health & performance.

## Slide 25: Six Characteristics of Adult Learners
Are self-directed.
Like to know why they need to learn
Prefer to learn in an environment that is characterized by mutual trust and respect
Learn from their own experiences and the experiences of others
Prefer knowledge that can be immediately applied
Learn better when they are actively involved in the learning process
NEEDED: A LEARNER-CENTERED APPROACH
Notes: Complete Narration: “Mature adults are different from children and young adults in their approach to learning.
First, adults are self-directed. They learn because they want to learn.
Second, adults like to know why they need to learn something. What is the relevance to their lives?
Third, adults prefer to learn in an environment that is characterized by mutual trust and respect.
Fourth, adults learn from their own experiences and the experiences of others. “Book knowledge” is not as meaningful.
Fifth, adults prefer knowledge that can be immediately applied to their work and to their lives.
Finally, adults learn better when they are actively involved in the learning process, not just receiving information.
For adults, what is needed is a learner-centered approach. In other words, instruction designed around the needs of the learner.”
_____________
Additional instructor note: Source: Knowles (1980).

## Slide 26: Effective Instructors
Respectful, personal relationships
High but realistic expectations
Actively engaged
Ensure that students are actively engaged
Recognize and reinforce success
See themselves as change agents
Notes: Complete Narration: “Effective instructors have several common characteristics and behaviors. They:
Have respectful, personal relationships with learners;
Have high but realistic expectations of learners;
Are actively engaged, and ensure that students are actively engaged;
Recognize and reinforce successful learning; and
They see themselves as change agents.
Part of being an effective change agent is realizing that most people are ambivalent about behavior change.
On the one hand, they want to look, feel, and perform better. On the other, it takes work and commitment to break bad habits and develop good ones.
___________
Additional instructor note: Source: Simons-Morton et al., 2012.
Review question: Q: We talked about learning and KSAs, but said that the ultimate goal of fatigue management could be expressed in two words. What were they? A: Behavior change.”

## Slide 27: Learning Principles Incorporated into FMP Modules
Clear objectives
Context & relevance
Overviews (“pre-organizers”)
“Chunking”
Spacing
Illustrations
Frequent practice
Feedback on performance
Review
Notes: Complete Narration: “Principles of learning have been incorporated into the ten FMP modules. As an instructor, you should be aware of these and use the same techniques in your teaching. Nine principles are briefly noted here. Clear objectives are stated for each unit of instruction. The context and relevance of each topic is also stated. Overviews, also known as “pre-organizers,” are provided so that students see the forest as well as the trees. “Chunking” means breaking up information so that it is presented in smaller pieces. “Spacing” means allowing for breaks between lessons. Module 3, for example, can be presented as four separate lessons. Illustrations are provided since much of learning is visual. Also provided are frequent opportunities for practice, and feedback on performance. Each module also includes a review to improve student retention.”
_________________
Additional instructor note: Source: Silber & Steinicki (1987). While these principles have been incorporated into the NAFMP modules, classroom instructors should conduct the training in consistent and supportive ways. For example, instructors should be prepared to explain the job-relevance of course material in their own words. They should be prepared to provide additional practice on course concepts if they find it is needed.

## Slide 28: Giving & Receiving Feedback
Feedback = knowledge of results
Feedback facilitates performance and behavior change
  Identifies present state of learning
  Highlights what needs to be learned
  Monitors progress
  Diagnoses problems
  Provides positive reinforcement for success
Tips for giving feedback:
  Sooner is better than later
  Emphasize the positive
  Consider it a two-way process
Notes: Complete Narration: “Feedback, or knowledge of results, is essential for effective learning. Feedback facilitates performance and behavior change. It identifies the present state of learning, highlights what needs to be learned, monitors progress, diagnoses problems, and provides positive reinforcement for success. Here are three tips for giving good feedback. Sooner is better than later. Emphasize the positive, and consider feedback to be a two-way process. Students learn from your feedback, and you learn from theirs.”
______________
Additional instructor note: There is a high relation between the amount of interaction and feedback in classrooms and the level of student interest in the material being taught.

## Slide 29: Creating a Positive Classroom Experience (1 of 2)
Physical setting and equipment are important
Take a learner-centered approach
Project enthusiasm
Ask questions and raise discussion points
Notes: Complete Narration: “There are many ways to create a positive classroom experience for students. First, the classroom physical setting and equipment are important. Use the best facility and equipment you have. Next, take a learner-centered approach, as we have already discussed. Project enthusiasm; it will rub off on students. Ask questions and raise discussion points to make the instruction interactive.”
_____________
Additional instructor note: The practices presented on this slide and the next one largely following from the learning principles already presented.

## Slide 30: Creating a Positive Classroom Experience (2 of 2)
Reinforce participation
Incorporate company examples
Maintain standards & accountability
Assess group & individual progress; adjust accordingly
Notes: Complete Narration: “Here are four additional ways to create a positive classroom experience. Reinforce student participation by responding positively to their questions and comments. Try to incorporate company examples into presentations and discussions. This will make the instruction more relevant and meaningful. Maintain standards and accountability. Students need to know the material, and there are quizzes and exams to ensure that. Use these tests and other feedback to continually assess group and individual progress. Adjust your instruction accordingly.”

## Slide 31: Webinars: Online “Classroom” Training
Webinar: Training or other meeting conducted online in real time
Students log on to company or service provider website from remote locations
Instructor role similar to classroom training, but via computer
Disadvantages:
  Requires existing webinar capabilities & IT support
  Instructor-student contact not face-to-face
  Student role is relatively passive
Notes: Complete Narration: “Webinars are training or other meetings conducted online in real time. Students log on to a company or service provider website from their remote locations. The instructor role in webinar training is similar to that in classroom training, but communication is via computer. Conducting FMP training by webinars might work for some companies, but there are disadvantages. It requires existing webinar capabilities and probably IT support. Instructor-student contact is not face-to-face. And the student role is relatively passive compared to both regular classroom and interactive web-based training. But webinars are a possible third instructional delivery option for some fleets.”
__________________
Additional instructor note: Graphic based on Driscoll, 2002. Webinars may not be an option for many companies, although more companies will acquire the capability in the future. Because of the disadvantages stated, webinars are not likely to be as instructionally effective as either classroom or web-based training.

## Slide 32: Incorporating Company Examples into Instruction
Consistent with learning principles:
  Context and relevance
  Learning more likely to be applied
  Reinforces company policies and practices
Two approaches:
  Company examples throughout instruction
  Supplemental lesson focusing on company examples
Cautions:
  Remember time constraints
  Should reinforce module content
  Respect individual privacy and confidentiality
Notes: Complete Narration: “As mentioned, you can and should incorporate company examples into the instruction. Incorporating company information is consistent with learning principles. It provides context and relevance. Learning is more likely to be applied if learners see the relevance to their work. It also helps to reinforce company policies and practices. Two approaches are to use company examples throughout the instruction or, alternatively, add a lesson focusing on company examples. A few cautions. Remember time constraints; if you are adding a lot of material, expect it to take more time. Your material should reinforce the main content of the module, not contradict it. If you are citing real company examples, be sure to respect the individual privacy and confidentiality of those involved.”
___________
Additional instructor note: As in other forms of training, training on company policies and practices will be more effective if it is planned and prepared. This would include specification of learning objectives and development of specific slides, handouts, or other courseware. Supplemental quiz and/or exam items might be appropriate.

## Slide 33: Maintaining Standards & Accountability in Driver Education Training
Be positive but rigorous
Set high expectations for classroom behavior & learning
Guard the integrity of module exams
  Students take exams individually
  Students do not see exams in advance
Maintain accurate records:
  Student attendance/participation
  Student exam scores
Notes: Complete Narration: “Some forms of driver training can take a casual approach, but the FMP driver training must have standards and accountability. Be positive but rigorous. Set high expectations for classroom behavior and learning. Guard the integrity of module exams. This means that students take the exams individually and that they do not see the exams in advance. You should also maintain accurate records of student attendance and of their exam scores. In contrast, Family Education is less rigorous. It should be more relaxed and fun. You may want to record attendance for your company’s records, but exam scores will not ordinarily be recorded.”
_________________
Additional instructor note: Maintaining accurate records and high standards for training not only improves employee performance and outcomes. It also helps to protect companies against litigation should there be a crash or personnel dispute.

## Slide 34: Quiz - Train-the-Trainer Overview
Which topic is covered in Module 3 (Driver Education) but NOT in Module 4 (Family Education)?
  Fatigue Crashes
  Scheduling and Hours-of-Service
  Health & Wellness
  Drugs and Medications
  Improving Sleep & Alertness.
Notes: Correct Answer: B

## Slide 35: Quiz - Train-the-Trainer Overview
Which is NOT a prerequisite for taking this Module 5 instruction?
  Successful completion of Module 3 (Driver Education)
  Successful completion of Module 4 (Family Education)
  Successful completion of at least one FMP module online (web-based)
  Prior experience as a Commercial Motor Vehicle (CMV) driver.
Notes: Correct Answer: D

## Slide 36: Quiz - Train-the-Trainer Overview
Which is NOT generally true of web-based training?
  Improved learning for most topic areas
  Easier to standardize than classroom training
  Increased training time required for most topic areas
  Easier tracking of exam scores and record-keeping.
Notes: Correct Answer: C

## Slide 37: Quiz - Train-the-Trainer Overview
The “A” in KSA stands for:
  Abilities
  Attitudes
  Achievement
  Associations.
Notes: Correct Answer: B

## Slide 38: Quiz - Train-the-Trainer Overview
Which best states the desired approach of FMP training?
  Learner-centered
  Organization-centered
  Prescriptive and compliance-based
  Focused on skill acquisition.
Notes: Correct Answer: A

## Slide 39: Driver Education Training, Part 1
Notes: Complete Narration: “This lesson overviews the Driver Education module and reviews the first half of its instruction.”

## Slide 40: Module 3 (Driver Education) Purpose & Features
Target audience: drivers
Duration: ~3 hours
Organization:
  Introduction
  4 main lessons
  Conclusion
Instruction should be spaced; i.e., only 1-2 lessons at a time
Instructional modes:
  Instructor-led PowerPoint (with instructor notes)
  Web-based
Tests:
  Checks on learning at end of most sections
  5-item quiz after each lesson
  30-item exam at module conclusion
Notes: Complete Narration: “The Driver Education module takes about 3 hours for completion. It is organized into an Introduction, four main lessons, and a Conclusion, which includes a review and module exam. The instruction should be spaced; that is, only one or two lessons should be taken at a time. You might, for example, cover one or two lessons each week until the instruction is complete. Instructional modes include instructor-led PowerPoints and web-based modules. Testing includes checks on learning at the end of most sections. There is also a 5-item quiz after each lesson and a 30-item exam at the end of the module.”

## Slide 41: Module 3 Learning Goals
(K) Recognize the major facts, concepts, procedures, and principles of driver fatigue
(S) Apply to:
  Lifestyle and behavior at home
  Lifestyle and behavior on the road
  Scheduling and HOS compliance
(A) Value sleep hygiene, wellness-related behavior, and alertness
(A) Value HOS compliance as being generally supportive of sleep hygiene
(A) Internalize the fatigue management safety culture
Notes: Complete Narration: “Module 3’s learning goals include knowledge, skills, and attitudes. Knowledge goals are to recognize the major facts, concepts, procedures, and principles of driver fatigue and related topics. Skill goals are to apply this knowledge to one’s lifestyle and behavior at home, on the road, and to scheduling and HOS compliance. The major attitude goal is to value sleep hygiene, wellness-related behavior, and alertness. Students should also value HOS compliance as being generally supportive of sleep hygiene. We hope that they will internalize the fatigue management safety culture.”
______________________
Additional instructor note: As already noted, most of the Module 3 training is directed toward knowledge goals. The general instructional strategy might be summarized as: Increase knowledge  Change attitudes  Change behavior  Improve health & performance.

## Slide 42: Module 3 (Driver Education) Overview
Introduction Introduction to Module Sleep, Alertness, Wellness, & Performance Lesson 1: Characteristics of Fatigue & Fatigue Crashes What is Fatigue? Fatigue Characteristics Fatigue-Related Crashes | Lesson 2: Sleep & Other Factors Affecting Alertness What is Sleep? Factors Affecting Alertness & Performance Individual Differences in Fatigue Susceptibility Lesson 3: Health, Wellness, Drugs, & Medications Health & Wellness Drugs & Medications | Lesson 4: Alertness & CMV Driving Improving Sleep & Alertness Scheduling & HOS Team Driving Conclusion Review Module Exam
Notes: Complete Narration: “Here are the Module 3 lessons and topics. Those covered in this train-the-trainer lesson are highlighted. Take a moment to review the lessons and topics.”
__________________
Additional instructor note: Before beginning the Module 3 review, you might ask your trainees about their recollections of the module. Which lessons and sections were most informative? Which were most difficult? Lesson 2 probably has the most fatigue-related material and covers the most fundamental concepts.

## Slide 43: Accelerated Review of Driver Education, Part 1
Next part of this lesson presents all content slides of the Driver Education Introduction, Lesson 1, and Lesson 2.
Narration will be abbreviated compared to the original.
Will provide higher-level comments on the instructional content as well as tips for effective teaching.
Testing:
  5-item quiz at the end of this Module 5 lesson
  Module 5 exam will include Module 3 fatigue-related content.
Notes: Complete Narration: “Next we will begin an accelerated review of the Driver Education module. The next part of this lesson presents all of the content slides of the Driver Education Introduction, Lesson 1, and Lesson 2. The narration will be abbreviated compared to the original Module 3 narration. It will provide higher-level comments on the instructional content as well as tips for effective teaching. There will be a 5-item quiz at the end of this Module 5 lesson, and the Module 5 exam will include fatigue-related content from Module 3.”

## Slide 44: Module 3: Driver Education
Notes: TtT Narration: “This is North American Fatigue Management Program Module 3, Driver Education.”

## Slide 45: Introduction
Notes: TtT Narration: “The Introduction includes basic information on the module and on sleep, alertness, wellness, and performance.”

## Slide 46: Introduction to Module
Topics:
North American Fatigue Management Program (NAFMP)
NAFMP training program
Module overview
Learning goals
Notes: TtT Narration: This is the introduction to the module.
__________________
Additional instructor note:
Learning objectives for this section include:
(K) Recognize NAFMP purpose.
(K) Recognize this module as part of a 10-module NAFMP training program.
(K) Understand general organization of module and major sections.
(K) Recognize general module learning goals (Knowledge, Skill, Attitudes)
(K) Recognize seven acronyms used in module.

## Slide 47: North American Fatigue Management Program (NAFMP)
Reality: Hours-of-Service (HOS) compliance is essential
Needed: A more proactive and comprehensive approach, centered around drivers
Notes: TtT Narration: Hours-of-Service compliance, for both the daily and weekly requirements, is essential for rest/sleep. However, a more proactive and comprehensive approach will support drivers in further managing other risk factors that contribute to fatigue. That’s why the North American Fatigue Management Program has been developed.”
______________________
Additional comment: The NAFMP and this module are supportive of HOS rules and their importance. .

## Slide 48: Module 3 Overview
Introduction Introduction to Module Sleep, Alertness, Wellness, & Performance Lesson 1: Characteristics of Fatigue & Fatigue Crashes What is Fatigue? Fatigue Characteristics Fatigue-Related Crashes | Lesson 2: Sleep & Other Factors Affecting Alertness What is Sleep? Factors Affecting Alertness & Performance Individual Differences in Fatigue Susceptibility Lesson 3: Health, Wellness, Drugs, & Medications Health & Wellness Drugs & Medications | Lesson 4: Alertness & CMV Driving Improving Sleep & Alertness Scheduling & HOS Team Driving Conclusion Review Module Exam
Notes: TtT Narration: “Here is an overview of the lessons and topics of this module. There is this introduction, four lessons, and a conclusion. Each lesson ends with a short self-test, and the module ends with a 30-item exam. Students must score 80% or higher on the exam to pass.”
_____________________
Additional instructor note: It is suggested that you “walk through” the lessons and topics to give students an advance overview.

## Slide 49: Module 3 Driver Education Learning Goals
Knowledge: Know major facts and principles of driver fatigue, alertness, sleep, & wellness.
Skill: Apply this knowledge to better manage demands of your work and life.
Attitudes: Value sleep, alertness, and wellness as major factors in your driving performance, safety, and happiness.
Notes: TtT Narration: “Here are general module learning goals, stated as “KSAs.” The knowledge goal is to know the major facts and principles of driver fatigue, alertness, sleep, and wellness. The skill goal is to apply this knowledge to better manage the demands of work and life. The attitude goal is to value sleep, alertness, and wellness as major factors in driving performance, safety, and happiness.”

## Slide 50: Acronyms
FMP = Fatigue Management Program
NAFMP = North American FMP
CMV = Commercial Motor Vehicle
REM = Rapid Eye Movement
OSA = Obstructive Sleep Apnea
BMI = Body Mass Index
HOS = Hours of Service
Notes: TtT Narration: “Here are some acronyms used in this and other NAFMP modules.”

## Slide 51: Sleep, Alertness, Wellness, & Performance
Topics:
Importance for CMV driver health & safety
What is alertness? What is wellness?
Good sleep: the key
Sleep hygiene & self-management
Notes: TLT Narration: “Our introduction continues with some basics on alertness, sleep, wellness, and driving performance. ”
_______
Additional instructor note:
Learning objectives for this section include:
(K) Recognize facts relating to the importance of sleep, alertness, and wellness for CMV drivers
(K) Recognize definitions of alertness, wellness, and sleep hygiene.
(K) Recognize relationships among sleep, alertness, performance, wellness, and happiness.
(A) Value the personal and safety benefits of sleep, alertness, and wellness.
(A) Accept personal responsibility to self-manage alertness.
Additional comment: The concepts presented in this section are general and intended to help establish driver appreciation of the importance of fatigue management, before proceeding to more substantive content.

## Slide 52: Importance to Health
Sleep is a biological need
Poor sleep contributes to:
  Cardiac conditions
  Diabetes
  Obesity
  Psychological disorders
  Other medical conditions.
Good sleep promotes wellness, high performance, and happiness
Notes: TtT Narration: “Sleep is a biological need and, therefore, lack of sleep has biological consequences. On the positive side, good sleep has biological and psychological benefits.”
_______________________
Additional comment: Research in recent years has greatly increased our knowledge of the importance of good sleep for health. The medical conditions listed are just a few of those associated with poor sleep.

## Slide 53: Importance to Safety
Falling asleep-at-the-wheel is a top cause of crash deaths for CMV drivers
Medical crises are another major cause of road deaths for drivers
An out-of-control truck or bus is a threat to anyone on our roadways.
One serious at-fault crash can end your career
It can even put a company out-of-business
Notes: TtT Narration: “Here we highlight the importance of sleep, alertness, and wellness for safety. Later slides will elaborate on the first two bullet points.”
_______________________
Additional information: Statement about asleep-at-the-wheel crashes is based on National Transportation Safety Board (NTSB), 1990 (to be discussed later in this module).

## Slide 54: Alertness, Wellness, & Sleep
What is alertness? Alert = awake + attentive
What is wellness? Wellness = physical, mental, emotional, & behavioral health and well-being
Good sleep is essential for both alertness and wellness.
Notes: TtT Narration: “This slide defines the terms “alertness” and “wellness” and shows their connections to good sleep.”

## Slide 55: Good Sleep: A Key to Performance & Happiness
Notes: TtT Narration: “This schematic presents the two general reasons for getting good sleep.
The first general reason involves alertness and performance.
The second general reason involves wellness and happiness.”
___________________
Additional comment: Research has proven the links between good sleep and alertness, performance, and wellness. The link to happiness is more subjective, but most people would agree that happiness is in part the result of having good health and being able to perform well.

## Slide 56: A Challenge & Responsibility
CMV driving is a challenging job under often-difficult conditions.
Each driver has a personal responsibility to wisely manage his or her own sleep, health, and lifestyle.
Sleep hygiene ≈ self-management.
Notes: TtT Narration: “The last slide of the Introduction acknowledges the challenges CMV drivers face. Each driver has a responsibility to meet these challenges by wisely managing his or her sleep, health, and lifestyle. This is termed sleep hygiene, and it is all about self-management.”
________________________
Additional comment: The terms “sleep hygiene” and “fatigue management” are almost synonymous. “Sleep hygiene” is used here more in the context of personal lifestyle, whereas “fatigue management” is used more in the context of transport operations. Both primarily involve behavioral self-management.

## Slide 57: Lesson 1: Characteristics of Fatigue & Fatigue Crashes
Notes: TtT Narration: “Lesson 1 covers the characteristics of fatigue and fatigue crashes. Topics include, “What is Fatigue?,”
Fatigue Characteristics, and Fatigue Crashes.“

## Slide 58: What is Fatigue?
Topics:
Fatigue elements/aspects
Two categories of fatigue:
  Internal
  Task-related
How fatigue progresses
Sleep as the principal antidote to fatigue
Notes: TtT Narration: “Here are the topics included in “What is Fatigue?”
_____________________
Additional instructor note:
Learning objectives for this section include:
(K) Recognize fatigue elements/aspects (“Fatigue involves . . . “).
(K) Recognize distinction between internal and task-related fatigue
(K) Recognize examples of internal and task-related factors affecting fatigue.
(A) Value sleep as the principal antidote to fatigue.

## Slide 59: Fatigue involves . . .
Decreased alertness
Decreased attention to the environment (vigilance)
Reduced performance
Reduced motivation
Irritability
Impaired judgment
Feelings of drowsiness
Notes: TtT Narration: “Fatigue is manifested in various ways, as seen in this slide. Decreased alertness and attention to the environment are the principal concerns in driving. Decreased attention to the environment is also called decreased vigilance.”
__________________
Additional comment: It is difficult to define fatigue exactly because of its many different sources and symptoms. The predominant features, however, are decreased alertness and feelings of drowsiness, and the resulting risk of falling asleep.

## Slide 60: Internal vs. Task-Related Fatigue
Two general categories of fatigue:
  Internal fatigue (sleep-related)
  Task-related fatigue (activity-related)
Both can affect your performance even if you don’t fall asleep-at-the-wheel
Reduced vigilance begins well before feelings of sleepiness
Notes: TtT Narration: “Just as fatigue has many symptoms, it also has many causes. The distinction between internal and task-related fatigue is introduced here. This distinction is useful for understanding the many factors affecting fatigue and alertness.”

## Slide 61: Internal vs. Task-Related Fatigue
Internal Factors
Individual Susceptibility
Amount of Sleep
Time-of-Day
Time Awake
Stimulants, Other Drugs
Health
Mood
Task-Related Factors
Time-on-Task
Task Complexity
Task Monotony
ALERTNESS
ATTENTION
DRIVING PERFORMANCE
Notes: TtT Narration: “This slide overviews internal and task-related factors affecting alertness. Internal factors include individual susceptibility; amount of sleep; time-of-day; time awake; stimulants like caffeine and other drugs; general health; and mood. Task-related factors include time-on-task (such as hours of driving), task complexity, and task monotony. All these factors affect alertness, which in turn affects attention to the environment and driving performance.”
______________________
Additional information: Figure adapted from Thiffault (2011). Most of the factors listed will be discussed in more detail in following slides. To stimulate discussion and thought, you might ask students which of the factors listed affect them the most. Which the least?

## Slide 62: SLEEP The Most Important Antidote to Fatigue
Notes: TtT Narration: “This slide reinforces the primary relationship between sleep and alertness, and between alertness and driving performance. Other factors are involved, but better sleep is the most important antidote to fatigue.”
____________
Additional instructor note: Optional check on learning: Q: What are the two main categories of fatigue?
A: Internal or sleep-related, and task-related, also called activity-related.”

## Slide 63: Fatigue Characteristics
Topics:
Acute vs. chronic
Signs and symptoms
Subjective vs. objective self-assessments
Health effects of sleep deprivation
Signs of chronic sleep deprivation
Sleep debts and recovery
Notes: TtT Narration: “Here are the topics within Fatigue characteristics.”
___________
Additional instructor note:
Learning objectives for this section include:
(K) Distinguish acute (short-term, “everyday”) from chronic (long-term) fatigue
(K) Identify general mental and physical warning signs and symptoms of fatigue.
(K) Recognize the fallibility of subjective self-assessments (e.g., many drivers don’t feel drowsy before falling asleep and can’t predict it happening).
(K) Recognize specific objective signs of fatigue while driving.
(K) Recognize performance effects, health effects, and everyday signs of sleep deprivation (or sleep debt).
(A) Value health- and safety-importance of fatigue warning signs.
(K) Recognize everyday signs of chronic sleep deprivation
(K) Recognize definitions of sleep deprivation, sleep debt, and recovery.
(K) Recognize incremental benefits of multiple nights recovery sleep.
(S) Apply knowledge of fatigue characteristics to personal fatigue management.

## Slide 64: Acute vs. Chronic Fatigue
Acute (short-term) fatigue:
  Experienced every day
  Reduced or eliminated by a night’s sleep or nap
  Caffeine and rest (without sleep) reduce mild fatigue
Chronic (long-term) fatigue:
  Afflicts many drivers and other busy people
  Due to inadequate sleep over a longer period
  Called sleep deprivation
  To recover, need a few nights of long, sound sleep
Notes: TtT Narration: “Fatigue management involves dealing with acute fatigue, which is short-term, everyday fatigue, and reducing chronic or long-term fatigue. It is our everyday behaviors, good or bad, that lead to longer-term consequences, good or bad.”

## Slide 65: Fatigue Signs & Symptoms (1 of 2)
Loss of alertness and attention
Wandering thoughts
Poor response, slow reactions
Distorted judgment
Loss of motivation
Notes: TtT Narration: “This slide and the next one provide a more detailed list of signs and symptoms of fatigue. They include loss of alertness and attention, wandering thoughts, poor response with slow reactions, distorted judgment, and loss of motivation.”

## Slide 66: Fatigue Signs & Symptoms (2 of 2)
Depression
Impaired memory
Reduced field-of-vision (“tunnel vision”)
Microsleeps
Little effect on purely physical tasks
Notes: TtT Narration: “Here are four additional signs and symptoms of fatigue. Reduced field-of-vision means that fatigued drivers spend less time looking at their mirrors than alert drivers do. In regard to the effect of fatigue on physical tasks, studies by the U.S. Army have found that sleep-deprived soldiers can still aim a rifle and accurately hit a target, but that they might choose the wrong target! Many “friendly fire” incidents in warfare are related to soldier fatigue.”

## Slide 67: Subjective vs. Objective Assessments
Driver Fatigue and Alertness Study:
Drivers subjectively rated their own alertness
Self-ratings were often inaccurate compared to objective measures
Drivers tended to rate themselves as more alert than they actually were
Self-ratings tended to be based on expectations:
  “I’ve been driving for a long time, so I must be tired”
  “I just started driving, so I couldn’t be tired”
Notes: TtT Narration: “To drive home the difference between subjective and objective assessments of fatigue, findings from three different studies are presented. This slide presents the findings from the joint U.S./Canada Driver Fatigue and Alertness Study. The study found little correlation between self-ratings of fatigue and objective measures.”
____________
Study cited: Driver Fatigue and Alertness Study, Wylie et al., 1996. Also see Wylie et al., 1997.
Additional information: The fact that drivers tend to rate themselves as more alert than they actually are is an example of the self-assessment bias in driving. One study showed that about half of all U.S. drivers consider themselves to be in the top 20%!

## Slide 68: Will you fall asleep in the next 2 minutes?
Stanford University Study:
Subjects sleep-deprived and asked to stay awake as long as possible
Periodically asked to predict whether they would fall asleep in the next 2 minutes
Onset of sleep correctly predicted 78% of the time
But 22% of the time it wasn’t
Large individual differences in ability to predict falling asleep
Notes: TtT Narration: “The Stanford University Study was more complicated but better shows the dangers of incorrect self-assessments of fatigue. In 22% of the cases where subjects fell asleep, they thought they would be able to stay awake. This is like a driver who thinks he can stay awake for another hour of driving. Further, there were large individual differences – many subjects were even worse.”
________________
Stanford University study cited: Itoi et al., 1993.

## Slide 69: Many Asleep-at-the-Wheel Drivers Never Feel Drowsy!
University of North Carolina Study:
Interviews with 312 motorists who had crashed after falling asleep at the wheel
Chart: 
| Not at all | Slightly | Moderately | Very | Don't Know
 | 0.23 | 0.21 | 0.16 | 0.37 | 0.03
Question: “How drowsy did you feel before you fell asleep at the wheel?”
Notes: TtT Narration: “In this study by the University of North Carolina, 23% of drivers who actually fell asleep while driving said afterwards that they felt “not at all drowsy” before their crash. Drivers should never count on “feeling drowsy” as a reliable indicator of fatigue risk.”
___________
UNC study cited: Stutts et al., 1999.

## Slide 70: But Only 11% Had 8+ Hours Sleep the Night Before!
Question: “How much sleep had you had the night before?”
Chart: 
| 8+ Hours | 6 to 7.9 | 4 to 5.9 | < 4 | Don't Know
 | 0.11 | 0.28 | 0.32 | 0.22 | 0.07
8+ Hours
Notes: TtT Narration: “The same study showed that inadequate sleep was a strong predictor of the fall-asleep crashes. Only 11% of the drivers had had 8 hours sleep and more than half, 54% had had less than 6 hours.”
_________________
Additional information: As previously, University of North Carolina Study: Interviews with 312 motorists who had crashed after falling asleep-at-the-wheel. Source: Stutts et al., 1999.

## Slide 71: Objective Signs of Sleepiness While Driving (1 of 2)
Eyes:
  Eyelid droop
  Loss of focus
Yawning
Thoughts:
  Wandering, disjointed
  Scattered, dreamlike visions
Head movements:
  Gentle swaying
  Jerks
Reduced field-of-view (“tunnel vision”)
Notes: TtT Narration: “Drivers should learn to pay attention to objective signs of their sleepiness. These include eyelid droop; loss-of-focus; yawning; wandering and disjointed thoughts; scattered, dreamlike visions; head swaying or jerking; and reduced field-of-view.”

## Slide 72: Objective Signs of Sleepiness While Driving (2 of 2)
Body movements:
  Fidgeting, shifting positions
  Adjusting windows, HVAC
Vehicle control:
  Weaving (progressive)
  Crossing rumble strip
  “Drift and jerk” steering
  Variable Speed
Delayed or incorrect responses
Microsleeps
Notes: TtT Narration: “Other objective, observable signs include those related to body movements and vehicle control. Fatigued drivers may also make delayed or incorrect responses, or have microsleeps.”
________________
Additional information: In a microsleep, the brain transiently goes into light sleep, even though the eyes may still be open. It is like a camera with no film. Information is coming in but it is not registering.

## Slide 73: Health Effects of Sleep Deprivation (1 of 2)
Increased blood pressure
Increased risk of heart disease
Gastrointestinal problems
Increased sick days
Increased calorie consumption
Weight gain
Notes: TtT Narration: “In addition to paying attention to signs of fatigue while driving, CMV drivers need to know the health effects of sleep deprivation and assess their own health from that perspective. Many of the health effects listed here and in the next slide are common among CMV drivers.”
________________
Principal source: Saltzman and Belzer, 2007.

## Slide 74: Health Effects of Sleep Deprivation (2 of 2)
Increased diabetes risk
Reduced immune system functioning
Irritability
Disrupts relationships
Worsens psychiatric conditions
Decreased quality of life
Notes: TtT Narration: “Additional health effects of sleep deprivation are listed here.”
___________
Principal source: Saltzman and Belzer, 2007.

## Slide 75: Are You Chronically Sleep-Deprived?
Do you fall asleep in 5 minutes or less?
Can you nap almost anywhere, any time?
Do you feel sleepy when you are bored?
Do you fall asleep easily while watching TV or in movies?
Do you ever fall asleep while stopped for traffic lights?
Notes: TtT Narration: “These five questions are posed to stimulate self-evaluation by drivers. In classroom instruction, you might ask students to privately write down their answers. While there is no scoring to the self-test, several “yes” answers probably indicates chronic sleep deprivation.”

## Slide 76: Sleep Debts
If you answered “yes” to the previous questions, you are probably chronically sleep deprived.
In other words, you have a sleep debt.
Like financial debt, you need to start paying it off.
Only one way to pay your debt  SLEEP!
Notes: TtT Narration: “Being sleep-deprived means having a sleep debt. Everyone understands financial debt. Thus, the analogy is a good way to motivate people to get more sleep.”
________________
Additional instructor note: The concept of sleep debt does not imply that people need to repay all the sleep they have lost over a lifetime. In most cases, several full nights’ sleep will restore full performance, though it will not eliminate long-term health effects of previous chronic sleep loss.

## Slide 77: Recovery from Sleep Deprivation
Begins following one night of good sleep.
May not be complete until you have several nights of good sleep.
Solution:
  Don’t get sleep deprived to begin with.
  Whenever possible, sleep until you wake up.
  Get more than one good night’s sleep on weekends.
To some extent, extra sleep can be “banked.”
Notes: TtT Narration: “Recovery from sleep deprivation begins with one night of good sleep, but may take several nights to be complete. It’s best if drivers get good sleep all week and don’t need to recover on weekends, but they should sleep the extra hours on weekends if they need it. The point about “banking” extra sleep is based on a U.S. Army study showing that subjects given extra hours of sleep prior to sleep deprivation did better during the sleep deprivation than those who just had normal sleep prior to the deprivation.”
___________________________
Instructor Note: Review question: Q: What happens to a drivers’ eyelids as he or she gets more and more drowsy? A: They droop.”
Additional information: Item on “banking” of extra sleep based on a sleep deprivation study conducted by the Walter Reed Army Institute of Research (Balkin, 2011). Subjects spending 10 hours a night in bed for a week before the sleep deprivation period were more alert than those who just followed their normal routine (7-8 hours in bed) prior to the sleep deprivation period.

## Slide 78: Fatigue-Related Crashes
Topics:
Characteristics
Ways fatigue causes crashes
How many fatigue-related crashes?
  Serious crashes
  Fatal-to-the-driver crashes
  Difficulties in estimating
Notes: TtT Narration: “Here are the topics in fatigue-related crashes.”
_________________
Additional instructor note:
Learning objectives for this section include:
(K) Identify typical characteristics of fatigue-related crashes.
(K) Recognize major risk factors (i.e., insufficient sleep, early morning driving).
(K) Recognize approximate percentages of fatigue-related crashes for major crash types (e.g., fatal-to-the-driver crashes).
(K) Recognize fatigue-related crashes as major threat to CMV drivers.
(K) Recognize complexities involved in determining number of fatigue-related crashes.
(A) Feel a personal concern regarding involvement in fatigue crashes, but confidence to address the threat through knowledge and wise behavior.

## Slide 79: Fatigue-Related Crashes
Usually single-vehicle road departures
Driver alone
Often on monotonous roads
Most in early morning, especially 2:00 am to 7:00 am
Usually serious crashes
Notes: TtT Narration: “This is the first of two slides on the typical characteristics of fatigue-related crashes.”
________________
Additional instructor note: These are typical characteristics, though almost any kind of crash can be fatigue-related. As a discussion topic, you might ask students whether they have ever “nodded off” at the wheel. Was it a microsleep as described in this instruction. Did they cross a rumble strip? Were they able to recover vehicle control in time to avoid a road departure?

## Slide 80: Principal Cause: Insufficient Sleep
Australian study found that truck drivers with less than 6 hours sleep were:
  3 times more likely to have a hazardous incident
  2.5 times more likely to nod off
Notes: TtT Narration: “From the causal perspective, the key characteristic of fatigue-related crashes is insufficient prior sleep. This slide reinforces information already presented in previous slides. HOS regulations give drivers the opportunity to receive adequate rest/sleep. As a discussion, you might ask students if they have been involved in, or are otherwise familiar with, a fatigue-related crash or incident. How does the information presented compare with their experience?”
________________
Australian study cited: Arnold and Hartley, 1998.

## Slide 81: 24-Hour Relative Rate
Chart: Hour-of-Day
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 1.2 | 1.7 | 2.3 | 3.5 | 3.9 | 4 | 2.8 | 1.4 | 0.5 | 0.3 | 0.3 | 0.4 | 0.4 | 0.3 | 0.4 | 0.6 | 0.8 | 0.7 | 0.4 | 0.3 | 0.2 | 0.5 | 0.8 | 0.5
Notes: TtT Narration: “This graph shows estimates of the relative rate of fatal fatigue-related crashes across the 24-hour day. All the hourly rates are divided by the 24-hour average so that the overall average in this graph is 1.0. Note the steep rise after midnight and the very high relative risk in the 3 to 5am period. There is a small bump in the mid-afternoon, but the main feature is the big peak in the early morning hours.”
__________________
Additional information: Figure shows estimated relative 24-hour fatal fatigue crash rate for large trucks. All days of the week are combined. These are only estimates because they are based in part on estimates of vehicle mileage exposure by hour-of-day. Data are normalized so 24-hour rate = 1.0. Source: Knipling, 2009. In the LTCCS (a different dataset than that presented in this slide), 62% of truck driver asleep-at-the-wheel crashes occurred in the two-hour period between 4:01am and 6:00am.

## Slide 82: Two General Ways Fatigue Can Lead to Crashes
Raise the risk of driving errors
Directly cause a crash (asleep at the wheel)
Timeline leading to a crash
DIRECT
CAUSES
Notes: TtT Narration: “This conceptual crash timeline illustrates two general ways that fatigue leads to crashes. It can be a risk factor setting the stage for a crash, or it can be a direct, immediate cause. The schematic is intended to help students understand the complexities of crash causation. Ask students if they have any questions about the schematic and be prepared to further explain it.”
________________
Graphic from Safety for the Long Haul; Large Truck Crash Risk, Causation, & Prevention (Knipling, 2009). Used with permission.

## Slide 83: How Many CMV Crashes are Fatigue-Related?
Large Truck Crash Causation Study (LTCCS):
In-depth investigations of ~1,000 serious large truck crashes
4% of truck crash involvements caused principally by truck driver asleep at the wheel
A larger number (13%) involved truck driver fatigue as an associated factor
Other crashes could have involved undetected fatigue
Notes: TtT Narration: “How many CMV crashes are fatigue-related? There is no single answer, but the LTCCS has provided meaningful estimates. It investigated large truck crashes resulting in serious injuries or fatalities. 4% were directly caused by truck driver asleep-at-the-wheel. But a larger number, 13%, involved fatigue as an associated factor. Many other crashes could have involved undetected fatigue, although, by definition, these cannot be documented.”
______________
Additional information: Police-reported statistics (including Police Accident Report-based databases like the General Estimates System (GES) and Fatality Analysis Reporting System (FARS) are generally underestimates because they are relatively superficial investigations. Source, Knipling, 2009; Starnes, 2006.

## Slide 84: Fatal-to-the-Driver Truck Crashes
1990 National Transportation Safety Board (NTSB) study of 182 fatal-to-the-driver large truck crashes
Most were single-vehicle road departures
In-depth investigation revealed fatigue to be a principal cause in 31%
Fatigue was the biggest cause
Cardiac and other medical crises are also major causes of such crashes
In 2010, more than 500 U.S. CMV drivers died in crashes
Notes: TtT Narration: “The crash statistic most meaningful to CMV drivers should be NTSB’s 1990 finding that 31% of large truck fatal-to-the-driver crashes had fatigue as a principal cause. Fatigue was the biggest single cause identified in the study. CMV fatal-to-the-driver crashes are not typical of CMV crashes in general, but they are the ones that hit closest to home.”
__________________
Source: NTSB, 1990. 56 of 182 crashes (31%) had fatigue as a principal factor.
Additional instructor note: The 31% statistic should not be generalized to larger crash populations like “all fatal truck crashes” or “all truck crashes.” Nonetheless, the statistic is important because it shows the importance of fatigue-related crashes for commercial drivers.

## Slide 85: Difficulties in Estimating Fatigue-Related Crashes
Driver:
  May be dead or severely injured
  May not know what happened
  May not admit to falling asleep
Fatigue contributes to crashes in subtle ways
Fatigue, distraction, and other causes may look the same
Many factors affect fatigue percentages
Notes: TtT Narration: “You have probably heard many different and wide-ranging statistics about the number of fatigue crashes. This slide reviews some of the reasons for the disparities in estimates. In regard to the final bullet, here are a few of the factors affecting the percentage of fatigue crashes identified in studies:
  Crash severity;
  Crash category (such as single- vs. multi-vehicle);
  Road type (such as freeways vs. other roads);
  Type of truck and operation;
  Depth and type of investigation; and
  Criterion; for example, fatigue as a primary, contributing, or associated factor.”
  _____________________
Instructor Note: Suggested check on learning: Q: Can you remember the peak time-of-day for fatigue-related crashes?
A: Between 2 and 7am.

## Slide 86: Lesson 2: Sleep & Other Factors Affecting Alertness
Notes: TtT Narration: “Driver Education Lesson 2 covers “What is Sleep?”, factors affecting alertness and performance, and individual differences in fatigue susceptibility.”

## Slide 87: What is Sleep?
Topics:
Key features of sleep
Types of sleep and sleep stages
Sleep inertia
Age differences in sleep
Factors affecting sleep quality
Notes: TtT Narration: Here are the topics within “What is Sleep?
___________
Additional instructor note:
Learning objectives for this section include:
(K) Identify key features of sleep (e.g., complex, not equal to rest).
(K) Recognize two types of sleep (“Regular,” REM) and their key characteristics.
(K) Recognize typical sleep patterns
(K) Recognize definition and characteristics of sleep inertia
(K) Identify age differences in sleep patterns
(K) Identify factors affecting sleep quality
(A) Appreciate the complexity and importance of sleep as an essential biological process.

## Slide 88: Key Features of Sleep
Sleep is necessary for performance and wellness, but no one knows exactly how or why!
Brain cells grow and connections are made during sleep
Sleep ≠ rest
Sleep is complex - The brain is not simply resting
Notes: TtT Narration: “The topic begins with some key, basic features of sleep.”
____________
Additional information: Sleep is studied in sleep labs where people are monitored for EEG (“brain waves”), heart rate, and breathing.

## Slide 89: Two Types of Sleep
“Regular” (Non-REM)
  Brain activity reduced but varied
  4 repeating stages of different depths
Rapid Eye Movement (REM)
  Brain active
  Eye movements
  Dreams
  Loss of muscle tone (~paralysis)
Notes: TtT Narration: “Understanding the structure of sleep is not essential for good sleep hygiene, but it is interesting and probably motivating for drivers. Knowing more about sleep probably motivates a person to get better sleep.”
_______________
Additional information: “Regular” (non-REM) sleep is known technically as “Slow Wave Sleep.” Each of the four stages has a distinct EEG pattern, but they are less like wakefulness than REM sleep is. Loss of muscle tone occurs in major muscle groups, but not in the muscles that move the eyes.

## Slide 90: Sleep States & Stages
Notes: TtT Narration: “This graph shows nightly sleep stages for a healthy young adult. Of course, different people have somewhat different patterns, and not every night is exactly the same. Older people are more likely to wake up during the night. Sleep lab studies provide us with this picture of sleep, but people have some awareness of their own sleep patterns. You might ask students if they think their own sleep matches this pattern. When during the night do they dream the most? When are they most likely to wake up during the night?”
_______________
Additional information: People are more likely to wake up in the second half of the night because the non-REM stages are lighter, as shown in the figure. In addition, there are individual differences in nightly sleep patterns, in part related to age.

## Slide 91: Sleep Inertia
Grogginess upon awakening
Can last 20 minutes or more
Can affect driving (especially before daybreak)
Caffeine helps
Notes: TtT Narration: “Sleep inertia is important because it can affect driving. Drivers should not try to drive immediately upon awakening; they should wait 20 minutes or more, preferably with some coffee or physical activity to help them awaken fully.”
__________
Additional information: Although sleep inertia can last 20 minutes or longer, more often it is about 10 minutes. It tends to be longer if a person is sleep-deprived and awakening from a deep recovery sleep. Some people experience more sleep inertia than others. Getting up before daybreak tends to make sleep inertia last longer because you are in a circadian low and/or are awakening from a deep sleep.

## Slide 92: Age Differences in Sleep
Adults need 7-8 hours
Teenagers and children need more
Older adults:
  Lighter sleep
  More easily disrupted
  May take more naps
  Not more likely to fall asleep at the wheel.
Young males (<30) are highest risk group for asleep-at-the-wheel crashes
But everyone can be at risk!
Notes: TtT Narration: “Most CMV drivers are middle-aged, so it is important for them to know something about age differences in sleep. As you get older, your sleep becomes more fragile, but that doesn’t seem to increase crash risks. While anyone can be at risk for a fatigue-related crash, young males under 30 appear to have the greatest risk. Everyone is at risk, though.”
______________
Additional information: People can survive for extended periods with inadequate sleep, but they cannot sustain optimal performance. Instead, they tend to get used to performing at sub-optimal levels and consider it normal.

## Slide 93: Factors Affecting Sleep Quality
Quantity affects quality
Other factors affecting quality:
  Bed comfort
  Darkness of room
  Time-of-day (best sleep during circadian valleys)
  Noise
  Temperature (cool is best)
  Anything else that might awaken you
Notes: TtT Narration: “Here are some factors affecting sleep quality. Most of them are “common sense,” but drivers may not fully appreciate the importance of some factors, such as room darkness and time-of-day.”
_____________
Additional instructor Note: Suggested review question on sleep: Q: What is sleep inertia, and how long does it last? A: The grogginess you feel upon awakening. It can last 20 minutes or longer.

## Slide 94: Factors Affecting Alertness & Performance
Topics:
Review: internal vs. task-related fatigue
Amount of sleep
Time-of-day (circadian rhythms)
Time awake
Time on-task
Other task-related and environmental factors
Task demands and performance
Notes: TtT Narration: “Here are the topics for “Factors affecting alertness and fatigue.”
______________
Additional instructor note:
Learning objectives for this section include:
(K) Identify key factors affecting alertness and performance [these are also causes of fatigue].
(A) Appreciate importance and value of getting sufficient sleep, and taking naps.
(K) Identify circadian high and low points of the 24-hour day and the overall circadian pattern.
(K) Recognize key features of circadian rhythms; basic patterns, effects of disruption, interactions with other factors.
(K) Identify the effects of task-related factors (e.g., time-on-task, monotony) on alertness.
(S) Apply information on factors affecting alertness and performance to job situations.
(K) Recognize the inverted-U-shaped relation between task demands (environmental stimulation) and performance.
(A) Accept the fact that fatigue stems from powerful biological drives and cannot be “willed” away.
(A) Value alertness-promoting lifestyles and work styles.

## Slide 95: Internal vs. Task-Related Fatigue (1 of 2)
Fatigue Category | General Source | Specific Factors
Internal Fatigue | Body Physiology | Amount of recent sleep Time-of-day Time awake Stimulants/other drugs General health Mood Individual differences in susceptibility
Task-Related Fatigue | Task (Driving, Other Work) | Time-on-task (e.g., hours driving) Task complexity Task monotony
Notes: TtT Narration: “This table overviews the many factors affecting alertness and fatigue. Here the emphasis is on internal factors.”
_____________________
Additional instructor note: Classifying fatigue sources into these two categories helps students to understand fatigue factors, but they should also understand that various sources combine to affect overall alertness and performance. In regard to effects, there are not two distinct types of fatigue.

## Slide 96: Internal vs. Task-Related Fatigue (2 of 2)
Fatigue Category | General Source | Specific Factors
Internal Fatigue | Body Physiology | Amount of recent sleep Time-of-day Time awake Stimulants/other drugs General health Mood Individual differences in susceptibility
Task-Related Fatigue | Task (Driving, Other Work) | Time-on-task (e.g., hours driving) Task complexity Task monotony
Notes: TtT Narration: “Here, task-related factors are highlighted.”

## Slide 97: Amount of Sleep
Last main sleep period (e.g., last night)
Previous sleep periods (e.g., the nights before; even previous weekend)
Naps
Notes: TtT Narration: “First and foremost is amount of sleep.”
___________
Additional instructor note: Subsequent slides will provide more detail on the first and last bullets. In regard to previous sleep periods, recall what we learned earlier about sleep debts and recovery.

## Slide 98: Cumulative, Progressive Effects of Different Amounts of Sleep on Performance
Chart: Days of Restricted Sleep
9 Hrs in Bed | 95 | 95 | 96 | 94 | 95 | 96 | 97 | 95
7 Hrs in Bed | 93 | 92 | 92 | 89 | 87 | 87 | 83 | 83
5 Hrs in Bed | 93 | 86 | 85 | 80 | 78 | 73 | 68 | 68
3 Hrs in Bed | 90 | 80 | 76 | 54 | 48 | 43 | 35 | 23
Notes: TtT Narration: “This shows the cumulative, progressive effects of different amounts of sleep. Not everyone is used to interpreting graphs, so this slide may be difficult for some students. Make sure that they understand the main point: everyday without adequate sleep lowers alertness and performance a little more.”
____________
Cited source: Balkin et al., 2000. This is a good example of a partial sleep deprivation study, where all subjects get some sleep but some get less than they need. Other studies show that any sleep in such studies is much better than no sleep. Performance measure was the Psychomotor Vigilance Test (PVT), a measure of visual attention which is frequently used in studies of alertness and fatigue. This work was conducted at the Walter Reed Army Institute of Research with commercial drivers as subjects.
Additional instructor note: Not everyone is used to interpreting graphs, so this slide may be difficult for some participants. Make sure they understand its key implications regarding the progressive effects of repeated sleep loss. As sleep deprivation (whether mild or severe) continues, sleep debts continue to grow and performance becomes worse.

## Slide 99: Naps
Best on-the-road countermeasure to drowsiness!
Can greatly improve alertness and performance for hours afterwards
NASA study of airline pilots: Planned naps reduced subsequent dozing by 50% and errors by 34%
Optimal nap duration: 20-40 minutes
Two cautions:
  Grogginess (sleep inertia) following naps, especially longer ones
  Possible disruption of sleep in next main sleep period, also especially for longer naps
Notes: TtT Narration: “Napping is an interesting topic for discussion. Many people love naps, but not everyone! Ask participants how often they nap and how beneficial they are.”
______________
Cited NASA Study: Rosekind et al., 1994. In this study, pilots were permitted to nap for up to 45 minutes; the average was 26 minutes. The 45-minute maximum was to ensure that pilots did not fall into deeper stages of sleep (i.e., Non-REM Stages 3 & 4), which would have increased the incidence and duration of sleep inertia upon awakening.

## Slide 100: Time-of-Day
Circadian rhythms:
Physiological; e.g.,
  Body temperature
  Hormone secretions
Controlled by the brain
Virtually all animals
Resistant to change (e.g., jet lag)
Occur even if you get plenty of sleep
Affected by light and dark
Notes: TtT Narration: “Time-of-day as a factor in alertness is another interesting topic. Do students find themselves sleepy at the same times every day? When is that?”
______________
Additional information: Circadian rhythms are affected by light and dark, but isolation studies show that they will last indefinitely even without daily light-dark changes. They tend to become slightly longer than 24 hours, however.

## Slide 101: Daily Circadian Rhythm
Chart: Circadian Rhythm of Alertness
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5
 | 10.5667 | 9.3333 | 8.1667 | 6.8333 | 5.6667 | 4.5 | 3.6667 | 3 | 2.8333 | 3 | 3.5667 | 4.4 | 5.6333 | 7.2333 | 8.9333 | 11.0333 | 13.2 | 15.1667 | 16.5 | 17.3333 | 17.8333 | 18 | 18 | 17.6667 | 17.1667 | 16.3333 | 15.3333 | 14.1667 | 13.1667 | 12.8333 | 13.3333 | 14.5 | 15.7333 | 16.6667 | 17.3333 | 17.9333 | 18.3333 | 18.3333 | 18.1667 | 18 | 18 | 17.8333 | 17.3333 | 16 | 14.6667 | 13.5 | 12.7333 | 11.7333
Notes: TtT Narration: “This is a schematic of daily alertness and arousal due to circadian rhythms. Ask if anyone can describe their own typical daily alertness changes.”
________________
Source: Knipling, 2009. Different physiological and performance measures follow slightly different patterns, but this shows the general pattern.

## Slide 102: Circadian Effects on Our Lives & Work
Peak performance times include:
  Mornings after 8 am
  Evenings
Valleys include:
  Deep valley: early mornings before sunrise
  Shallow dip: early- to mid-afternoon (e.g., after lunch)
Circadian disruption (e.g., time zone and shift changes) can be difficult
Sleep loss makes circadian valleys deeper
Some people are “larks” or “night owls”
Performance is almost always better during peak periods
Notes: TtT Narration: “This slides reinforces the schematic and provides additional information.”
_______________
Additional instructor note: In discussions, a few people may claim that they perform better during the overnight hours than during the daytime. Only rarely is this true. Objective measures almost always show the same predictable variations in performance over the 24-hour day, although details may vary among people.

## Slide 103: Time Awake
16 hours awake: “Nature’s HOS rule”
Lab study compared alertness effects of long times awake to those of alcohol (BAC):
  17+ hours awake ≈ 0.05% BAC
  24+ hours awake ≈ 0.1% BAC
Interactions:
  Naps
  Circadian effects
  Sleep inertia (grogginess)
16 HOURS
AWAKE
Notes: TtT Narration: “Time awake is another topic where people can compare their own lives to “the textbook.” Do students find that they do indeed get sleepy each day after about 16 hours awake?”
_______________
Cited study: Dawson and Reid, 1997. Note that, all things considered, alcohol is still generally riskier than drowsiness, even if alertness/performance levels are the same. Unlike fatigue, alcohol increases risk-taking and affects motor coordination in addition to affecting alertness.

## Slide 104: Time-on-Task (Hours Driving or Working)
Some studies show increased crash risks after long hours of driving
Factors which increase time-on-task effects:
  Task difficulty
  Task monotony
  Other alertness factors (those already discussed)
Countermeasure: take breaks (with nap if possible)
Notes: TtT Narration: “Task-related and environmental factors. You might ask students which factors affect them the most.”

## Slide 105: Task Demands & Performance:
Performance
Task Demands
Notes: TtT Narration: “The inverted U relationship between task demands and performance is conceptual and may be difficult for some students. But understanding the concept may help drivers to better manage their driving workloads. To illustrate work overload while driving, ask students if they ever turn off their radios when they are in heavy traffic or unfamiliar locations. That’s sometimes a good thing to do, because it reduces work overload.”
_______________________
[Star appearance and movement will coordinate with narration]:
[No star] - “The nature of the task you are performing affects your performance. This graph shows performance as a function of task demands.
[Monotony star] - “Let’s explore this general relationship using a few examples. The yellow star shows likely performance if a task is extremely undemanding. If a task is very undemanding, it is boring. Monotony takes hold. You might get drowsy and your performance might be low. When could this happen in driving? One example would be a long drive through featureless terrain, like a desert.”
[Work overload star] - “At the other extreme, when a task is overly demanding, such as driving in very heavy traffic for several hours, you might get stressed out and your performance might be low as well. As you can see, the two opposite situations can both lead to poor performance.”
[Happy medium star]- “Your performance is likely to be best when the task is moderately demanding. The activity keeps you awake but doesn’t stress you out. The yellow star here shows high performance on a moderately demanding task ”
Additional instructor Note: This general “inverted U” relationship is seen in many areas of human performance. For example, sports competition is boring if the competition is too easy, but frustrating if it is too difficult. The optimal situation is moderate difficulty.
Optional section check on learning: Q: In general, what is the best length for a nap? A: 20 to 40 minutes.

## Slide 106: Environmental Factors Affecting Alertness
Road conditions
Weather
Environmental stress (heat, noise, vibration)
Vehicle design
Light/dark
Social interaction
Other stimulation
Notes: TtT Narration: “Here are various environmental factors affecting alertness.”
________________________
Additional information: Vehicle design factors in driver alertness, performance, and comfort are addressed by the field of ergonomics. This includes seat comfort (e.g., air-cushion vs. conventional), safety belts, visibility of mirrors, interior and exterior lighting, and so forth.

## Slide 107: Individual Differences in Fatigue Susceptibility
Topics:
Evidence
Causes
Sleep disorders:
  Obstructive Sleep Apnea
  Insomnia
  Other:
    Narcolepsy
    Restless Leg Syndrome
Are you highly susceptible?
Notes: TtT Narration: “Here are the topics within individual differences in fatigue susceptibility.”
__________________
Additional instructor note:
Learning objectives for this section include:
(K) Recognize the fact and importance of large individual differences in fatigue susceptibility.
(K) Recognize major causes of individual differences
(K) Recognize definition and characteristics of obstructive sleep apnea (OSA).
(K) Identify OSA risk factors and their negative association with wellness and safe driving.
(K) Identify typical OSA screening methods and treatments (i.e., CPAP).
(K) Recognize approximate incidence of OSA in CMV drivers.
(A) Appreciate value of OSA screening for self and drivers in general.
(K) Recognize definition, characteristics, and treatments for insomnia.
(K) Recognize definitions and key characteristics of other sleep disorders; e.g., narcolepsy, restless leg syndrome.
(K) Recognize reasons why people may not know whether they are highly susceptible.
(S, A) Honestly self-assess fatigue susceptibility, and appreciate its importance and value.

## Slide 108: Evidence of Individual Differences 10 Truck Drivers from Safety Study
Chart: Driving Incidents with High Drowsiness
| A | B | C | D | E | F | G | H | I | J
 | 0.026 | 0.013 | 0.006 | 0.003 | 0.002 | 0.001 | 0 | 0 | 0 | 0
Notes: TtT Narration: “This bar graph illustrates large differences among ten drivers. Point out that drivers G, H, I, and J all had zero high drowsiness incidents.”
___________________________
Data from Hickman et al., in press. Also based on Knipling, 2009. Many different studies have shown similar variations among drivers in their frequency of drowsiness.

## Slide 109: Individual Differences in the Driver Fatigue & Alertness Study
Chart: 
| Drivers | Drowsy Periods
 | 0.86 | 0.46
 | 0.14 | 0.54
Notes: TtT Narration: “This graph, taken from a different study, illustrates the same point in a different way. As with other graphs, some students might not grasp it immediately. Try to walk them through it until it is clear.”
_________________
Source: Wylie et al., 1996.

## Slide 110: What Causes Individual Differences in Fatigue Susceptibility?
Differences in sleep-related behaviors
Differences in health and fitness
Medications
Natural, genetic variations
Sleep disorders; most important: Obstructive Sleep Apnea (OSA)
Notes: TtT Narration: “Five types of causes of individual differences in fatigue susceptibility.”
_____________
Note: A general reference relating to driver medical qualifications, including OSA, is the FMCSA Medical Examiner Handbook.

## Slide 111: What is Obstructive Sleep Apnea (OSA)?
Apnea = stoppage of breathing lasting 10+ seconds
OSA = breathing stops repeatedly during sleep due to closures of the upper airway
Apnea rate per hour:
  <5 = normal
  >5 = OSA
OSA severity (mild, moderate, severe) based on rate
Some people with severe OSA can have 100 per hour!
© ResMed 2011 Used with Permission
Notes: TtT Narration: “OSA is a major concern for the industry, and for many drivers. Here OSA is defined and briefly described.”
_____________
Additional instructor note: Modules 7 and 8 contain extensive information on OSA, including video illustrations.

## Slide 112: OSA Risk Factors & Warning Signs
Higher risk:
  Obese and overweight individuals
  Male
  40+ years old
  Large neck size (>17” for men, >16” for women)
  Recessed chin, small jaw, or large overbite
  Family history
Physical effects and warning signs:
  Excessive daytime sleepiness and reduced performance
  Snoring
  High blood pressure (hypertension)
  Diabetes
  OSA tends to worsen obesity
Notes: TtT Narration: “OSA risk factors, physical effects, and warning signs. Instructors should not pry into students’ medical conditions, but often students will want to talk about them. You could ask if anyone in the class would like to talk about experiences with OSA. This might include symptoms, diagnosis, and treatment.”
____________
Additional information: One study (Xie et al., 2011) found that obese individuals (BMI > 30) had a 29-fold increased OSA risk compared to non-obese individuals. Nonetheless, some people with normal weights can have OSA. OSA risk strongly correlates with obesity and other warning signs, but OSA must be confirmed by a sleep lab study, discussed in subsequent slides.

## Slide 113: OSA & Driving
Studies of non-CMV drivers suggest 2 to 7-fold crash risk
Can result in medical disqualification (although often undiagnosed and undetected during qualification process)
Estimated 28% of CMV drivers have mild to severe OSA
Notes: TtT Narration: “Here are some facts about OSA and driving. Although the 2-to-7 fold risk estimate is based on non-CMV drivers, the elevated risk applies to CMV drivers as well.”
___________
Additional information: 2-7 fold crash risk estimate from Sassani et al. (2004). Relative crash risk studies involving CMV drivers have not been definitive and thus are not cited here. The 28% incidence statistic is from Pack et al., 2002.

## Slide 114: OSA Screening & Treatment
Screening
  Assessment of risk
  Sleep study
Treatments can be very effective if followed; e.g.,
  Continuous Positive Airway Pressure (CPAP) machine
  Weight reduction and behavioral changes
NAFMP Module 8 provides additional driver education
Notes: TtT Narration: “OSA screening and treatments. Treatments must be followed to be effective. Suggest that drivers also take Module 8 for additional information on OSA.”
___________________
Additional instructor note: Treatments are examples. There are others. CPAP is effective, but only if the treatment is followed faithfully. One night of non-use results in sleepiness the following day. As a discussion topic, you might ask if any students use CPAPs. Do they work? What are the challenges using them. Many people will say that their health and life quality have been greatly improved by CPAP use, even if it is difficult.

## Slide 115: Insomnia
Inability to fall or stay asleep
Very common, often related to stress
Usually not a medical condition, though it can be
Irony: Sleeping pills are often used to treat insomnia, yet insomnia can be related to excessive use of sleeping pills
Steps to reduce insomnia:
  Reduce caffeine intake (amount and timing)
  Have a wind-down routine
  Completely darken bedroom
Notes: TtT Narration: “Insomnia. This is yet another topic where students may want to talk about their experiences. The most important question is, “What works to reduce it?”
__________________
Additional information: The most important question about insomnia is, “What works to reduce it? Sleep-related behaviors such as caffeine use are most important. Individuals with chronic insomnia should see their physicians, however.

## Slide 116: Other Sleep Disorders
Restless Leg Syndrome (RLS)
  Afflicts ~5% of adults
  Usually not serious
  Tingling or other leg discomfort causes excessive movement
  Cannot relax to sleep
Narcolepsy
  “Seizure of numbness”
  Fall asleep suddenly
  Lasts a few seconds to 30 minutes
  Extremely dangerous, but rare
Others (e.g., sleepwalking, abnormal circadian rhythms)
Notes: TtT Narration: “Other sleep disorders include RLS and Narcolepsy.”
___________
Additional information: Both Restless Leg Syndrome and Narcolepsy are treatable with drugs. Individuals with Narcolepsy would not likely be commercial drivers. It is a neurologic condition, not a breathing disorder like OSA.

## Slide 117: General Symptoms of Sleep Disorders
Different sleep disorders have different symptoms
Excessive daytime sleepiness
Extremes in ability to go to sleep:
  Able to sleep almost immediately, almost anywhere
  Unable to sleep for a long time, even under ideal conditions
Loud, irregular snoring, especially with gasping
Notes: TtT Narration: “General sleep disorder symptoms. Most of these apply to OSA especially.”

## Slide 118: Are you highly susceptible to fatigue?
Most highly susceptible people don’t know it!
Reasons:
  Self-assessment bias
  Most driving is solitary
  Subjective self-assessments of alertness are poor
  Most sleep disorders are undiagnosed
Solution (be honest with yourself):
  Pay attention to:
    Signs of chronic fatigue
    Objective signs of fatigue while driving
    OSA symptoms and risk factors
  Consider any asleep-at-the-wheel incident to be a red flag!
Notes: TtT Narration: “The final slide of this section encourages students to try to assess their own fatigue susceptibility. There is no simple way. For starters, people have to be honest with themselves. This ends Part 1 of the Module 3 review. Next you will have a 5-item quiz on the Module 3 Part 1 material.”
___________
Additional instructor Note: Based on the LTCCS (e.g., Starnes, 2006) and other studies, the fatigue involvement rate in single-vehicle crashes is at least ten times that of multi-vehicle crashes. Any driver involved in a single-vehicle crash should carefully ask himself or herself whether fatigue was a factor.
Optional check on Learning: Q: In this section we listed five causes of individual differences in fatigue susceptibility. Can you remember three of them? A: Differences in sleep-related behaviors, differences in health and fitness, medication use, natural genetic variations, and sleep disorders.”

## Slide 119: Quiz - Driver Education Review: Part 1
Complexity and monotony are two factors in:
  Sleep hygiene
  Wellness
  Sleep-related (internal) fatigue
  Task-related fatigue.
Notes: Correct Answer: D

## Slide 120: Quiz - Driver Education Review: Part 1
One good night’s sleep can greatly reduce:
  Chronic (long-term) fatigue
  Acute (short-term) fatigue
  Accuracy of self-assessments of alertness
  Health effects of sleep deprivation.
Notes: Correct Answer: B

## Slide 121: Quiz - Driver Education Review: Part 1
Which statement is NOT true about asleep-at-the-wheel crashes?
  Usually single-vehicle road departures
  Generally more severe than other types of crashes
  Older drivers are at greatest risk
  Often associated with insufficient prior sleep.
Notes: Correct Answer: C

## Slide 122: Quiz - Driver Education Review: Part 1
Which statement is true about circadian rhythms?
  Controlled by the brain
  Unaffected by dark and light
  For most people, evenings (e.g., 6:00 to 10:00pm) are a circadian valley
  “Night owls” actually perform better during the overnight hours than during the daytime.
Notes: Correct Answer: A

## Slide 123: Quiz - Driver Education Review: Part 1
In the Driver Fatigue and Alertness Study (DFAS, Wylie et al., 1996), the worst 14% of the drivers in the study had what percentage of all the drowsy episodes?
  14%
  28%
  54%
  92%.
Notes: Correct Answer: C

## Slide 124: Driver Education Training, Part 2
Notes: Complete Narration: “This lesson reviews the second half of the Driver Education module.”

## Slide 125: Module 3 (Driver Education) Overview
Introduction Introduction to Module Sleep, Alertness, Wellness, & Performance Lesson 1: Characteristics of Fatigue & Fatigue Crashes What is Fatigue? Fatigue Characteristics Fatigue-Related Crashes | Lesson 2: Sleep & Other Factors Affecting Alertness What is Sleep? Factors Affecting Alertness & Performance Individual Differences in Fatigue Susceptibility Lesson 3: Health, Wellness, Drugs, & Medications Health & Wellness Drugs & Medications | Lesson 4: Alertness & CMV Driving Improving Sleep & Alertness Scheduling & HOS Team Driving Conclusion Review Module Exam
Notes: Complete Narration: “Here again are the Module 3 lessons and topics. Those covered in this train-the-trainer lesson are highlighted. Take a moment to review the lessons and topics.”

## Slide 126: Accelerated Review of Driver Education, Part 2
Next part of this lesson presents all content slides of the Driver Education Lesson 3, Lesson 4, and Conclusion.
Narration will be abbreviated compared to the original.
Will provide higher-level comments on the instructional content as well as tips for effective teaching.
Testing:
  5-item quiz at the end of this Module 5 lesson
  Module 5 exam will include Module 3 fatigue-related content.
Notes: Complete Narration: “Now we will resume our accelerated review of the Driver Education module. The next part of this lesson presents all of the content slides of the Driver Education Lesson 3, Lesson 4, and Conclusion. The narration will be abbreviated compared to the original Module 3 narration. It will provide higher-level comments on the instructional content as well as tips for effective teaching. There will be a 5-item quiz at the end of this Module 5 lesson, and the Module 5 exam will include fatigue-related content from Module 3.”

## Slide 127: Lesson 3: Health, Wellness, Drugs, & Medications
Notes: TtT Narration: “Lesson 3 addresses Health, Wellness, Drugs, and Medications.”

## Slide 128: Health & Wellness
Topics:
Importance
Personal keys to wellness
Diet and nutrition
Exercise
Weight
Smoking
Stress
Personal relationships
Steps in behavior change
Notes: TtT Narration: “Here are the topics within “Health and wellness.”
_____________________
Additional instructor note:
Learning objectives for this section include:
(K) Recognize personal benefits of health and wellness
(K, A) Recognize and value five personal keys to wellness
(K) Recognize the approximate incidence of major health threats (e.g., being overweight, smoking) among CMV drivers.
(K) Recognize societal and individual effects of poor health behaviors (e.g., poor diet, lack of exercise, being overweight, smoking, stress, poor personal relationships).
(K) Recognize behaviors supportive of wellness; i.e., good diet, physical activity, normal weight, not smoking, stress management, positive relationships.
(K) Recognize five steps to behavior change.
(S) Apply knowledge of health and wellness to personal self-management.
(A) Value wellness and wellness-enabling behaviors.

## Slide 129: Health & Wellness: What’s in it for you?
How you look and feel
Alertness and performance while driving
Longevity on the job
Increased life expectancy
Some unhealthful behaviors are about twice as common among commercial drivers as in general population
Notes: TtT Narration: “Health and wellness – what’s in it for you? We want drivers to feel ownership of both the problem and the benefits of improvement.”
___________
Additional information:
Study cited: Roberts and York (2000), study sponsored by the U.S. DOT and performed by the National Private Truck Council (NPTC). Examples of percentages cited in report:
Smoking: ~50% of truck drivers versus ~25% of general population.
Overweight: >70% of truck drivers versus ~32% of general population [in 1994; greater today]
High blood pressure: ~44% of truck drivers versus ~26% of general population.
Preliminary data from a 2011 National Institute of Occupational Safety & Health (NIOSH) survey:
Smoking: 46% of truck drivers versus 21% of the U.S. population
Obese: 65% vs. 34%
“Fair” or “poor” health (self-reported): 18% vs. 10%.
Diabetes: 14% vs. 8%.

## Slide 130: Personal Keys to Wellness
Notes: TtT Narration: “These five personal keys to wellness are addressed individually in the slides that follow.”

## Slide 131: Diet & Nutrition (1 of 2)
Too much food, fat, salt
CMV drivers’ favorite foods: steak & burgers
Leading causes of death related to what people eat
Many fried and processed foods are not healthful
Good foods: grains, fruits, vegetables, low-fat milk products, lean meats, fish, nuts
Notes: TtT Narration: “Diet and nutrition. This and other keys to wellness are covered with a few points about the problem and some strategies for improvement.”
____________________________
Survey cited: Holmes et al. (1996), in Krueger et al., (2007)

## Slide 132: Diet & Nutrition (2 of 2)
Simple Behavioral Goals:
Strive for Five: 5 servings of fruits or vegetables daily
Replace bad fats (e.g., chips) with good fats (e.g., nuts)
Replace bad carbs (e.g., sweets, potatoes) with good carbs (e.g., whole grains)
Replace sweet drinks with water
Notes: TtT Narration: “Some simple and specific behavioral goals. Ask drivers whether they make a focused effort to eat more fruits and vegetables. Does it work?”

## Slide 133: Exercise (1 of 2)
Recommendation:
  2.5 hours per week aerobic exercise (e.g., fast walking)
  + Muscle-strengthening workouts twice a week (e.g., weightlifting, pushups).
Benefits:
  Improves digestion
  Reduces weight
  Raises energy level, mood, self-esteem
  Reduces stress
  Improves sleep (if 3+ hours before sleep)
  Reduces disease risks
Notes: TtT Narration: “Commercial driving is usually sedentary, and lack of exercise is a major concern expressed by drivers. Aerobic exercise is most important, but adults need muscle-strengthening workouts as well.”
____________
Exercise recommendations from the Centers for Disease Control and Prevention.

## Slide 134: Exercise (2 of 2)
Strategies:
10-minute walks twice or more per day
Work out more vigorously on weekends
Take exercise equipment with you on trips
Keep a record of your exercise
Set daily and weekly goals
Find out what you like and do it!
Notes: TtT Narration: “Strategies for getting more exercise. Do any students keep a record of their exercise? Keeping a record is an important “starter” behavior.”
_____________
Additional information: Walking around a tractor-semitrailer 50 times = 2 miles!

## Slide 135: Weight
  CMV drivers:
    ~50% are obese
    Another ~25% are overweight
Body-Mass Index (BMI)
  Weight/Height2 × 703
  Scale:
    <25 = normal
    25-30 = overweight
    >30 = obese
Being overweight/obese increases risks of heart disease, high blood pressure, Diabetes, OSA, other injuries, and some cancers
Strategies: diet and exercise
Notes: TtT Narration: “Here are some driver weight statistics and effects. If students want to calculate their own BMIs, you may need to help them with the math.”
______________
Weight studies: Korelitz et al. (1993), Hickman et al. (in press).
Additional information: Preliminary data from a 2011 National Institute of Occupational Safety & Health (NIOSH) survey shows even higher percentages for CMV driver overweight and obesity: 89% overweight vs. 68% of U.S. adults; 65% obese vs. 34% of U.S. adults.
Determining BMI in the metric system is much easier; simply take your weight in kilograms and divide it by your height in meters, squared.
Obese drivers are less likely to wear safety belts, perhaps because belts are uncomfortable for them. This puts them at even greater risk. Source: Wiegand et al., 2008.

## Slide 136: Smoking & Other Tobacco Use
Leading preventable cause of disease, death, and disability
~20% of Americans smoke, but nearly half of CMV drivers do
Causes lung cancer, COPD and other lung diseases, heart disease, and many other medical conditions
>$1,000 per year in medical costs for each smoker
Reduces oxygen flow to the brain; worsens OSA
Strategy: QUIT!!!
  See your doctor
  Call 1-800-QUIT-NOW
  Click www.smokefree.gov
Notes: TtT Narration: “Smoking and other tobacco use. If a person smokes, quitting should be their #1 health priority.”
______________
Additional information: Preliminary data from a 2011 National Institute of Occupational Safety & Health (NIOSH) survey: 46% of surveyed CMV drivers smoked, versus 21% of U.S. adults. In a survey of nearly 3,000 truck drivers, Korelitz et al. (1993) found that 54% smoked, compared to 28% of all U.S. males and 25% of females at the time. Medical cost data from American Lung Association.
COPD = Chronic Obstructive Pulmonary [lung] Disease

## Slide 137: Stress (1 of 2)
Symptoms:
Headaches
Sleep disturbances
Difficulty concentrating
Short temper
Upset stomach
Job dissatisfaction
Low morale
Notes: TtT Narration: “Commercial driving can be stressful! One study found truck driver stress to be higher than 90% of the population. Here are some symptoms.”
____________
Study cited in narration: Orris et al, 1997.

## Slide 138: Stress (2 of 2)
Strategies:
Positive outlook and behaviors
Balance between work and personal life
Pursue personal interests
Support network
Try to improve job environment
Get serious about relaxing!
  Relaxation breathing
  Short walks
  Meditation
  Reading
  Find method that works best for you
Notes: TtT Narration: “There are effective strategies to deal with stress. Many also improve overall health and wellness.”

## Slide 139: Personal Relationships: Family & Friends
Driver survey: Lack of family time was the biggest single health and wellness concern
Driver personal and family problems sometimes lead to unsafe driving and accidents
Strategies:
  Keep in touch, communicate
  Value and foster each relationship
  Do fun things together
  Be positive
  Show support
Notes: TtT Narration: “Personal relationships is the last of the five keys to wellness. Family and other personal problems affect many drivers. This slide offers some strategies.”
______________
Additional information. Survey: Roberts & York, 2000. Top ten driver health concerns based on survey of 448 CMV drivers (in order): lack of family time, lack of exercise, weight, fatigue, poor diet, stress, lack of sleep, heart disease, cancer, high blood pressure. Of course, survey responses are subjective.

## Slide 140: Steps to Behavior Change
Aware, thinking
of change
Unaware
of
problem
Taking action
Planning
to change
Sustaining action
Health, Wellness, Alertness, Performance
Notes: TtT Narration: “Here are steps to behavior change. Although five specific steps are shown, the actual process may be more gradual and continuous. Ask students whether they have changed any of their health-related behaviors in similar ways.”
_______________
Additional instructor note: Module 5 contains much more detail on the five steps to behavior change. You may want to discuss some of those details in class.
Optional check on learning: Q: Earlier, we talked two different kinds of exercise you should engage in. What were they?
A: Aerobic and muscle-strengthening. Note: A weekly goal for aerobic exercise is 2.5 hours.

## Slide 141: Drugs & Medications
Topics:
Caffeine
Other stimulants
Sleep aids: supplements and herbal teas
Sleeping pills
Side effects of other medications
Alcohol
Notes: TtT Narration: “Here are the topics in “Drugs and medications.”
_____________
Additional instructor note:
Learning objectives for this section include:
(K) Recognize effects of caffeine
  Negative effects on sleep
  Correct use of caffeine to support alertness.
(K) Recognize negative effects of stimulants (e.g., Dexedrine)
(K) Recognize main categories of sleeping pills (hypnotics)
(K) Recognize supplements and herbal teas used as sleep aids.
(K) Recognize correct use of sleeping pills.
(K) Recognize negative effects of alcohol on sleep.
(A) Value moderation in use of alcohol, sleep aids, and caffeine.
Additional information: Krueger et al. (2011) is a good, general source of information of the effects of drugs and medications on CMV driver health and performance.

## Slide 142: Caffeine
The most widely used stimulant
In coffee, tea, most sodas, energy drinks, some medications
Generally safe and healthy if used in moderation
Improves alertness and performance
Effects and tolerance vary widely
Effective fatigue countermeasure, but not a substitute for sleep
Notes: TtT Narration: “Caffeine basics. Students may be surprised to learn that caffeine is not unhealthful if used in moderation.”
_____________
For additional information on the behavioral effects of caffeine and other drugs, see Krueger et al. (2011).

## Slide 143: Using Caffeine
Alerting effects:
  Begin in ~20 minutes
  Peak in 60-90 minutes
  Can last for hours
Caffeine content in coffee varies widely
Tea and most cola drinks have about ½ the caffeine of coffee
Large individual differences in the time required to metabolize caffeine
Drink in small sips to “nurse” the cup over a longer period
Notes: TtT Narration: “Using caffeine. Once again there are large individual differences. Most of the discussion relates to coffer, but you might mention caffeinated gum. It puts caffeine into the blood stream faster than drinking coffee, tea, or cola.”
_________
Principal source: Krueger et al. (2011).

## Slide 144: Caffeine & Sleep
Like any stimulant, caffeine makes sleep more difficult
Generally, avoid caffeine within 6-8 hours of main sleep period
Effects vary - some people are even more sensitive
If you have trouble going to sleep:
  Reduce caffeine intake
  Increase time between last dose & bedtime
Notes: TtT Narration: “Caffeine and sleep. Anyone using caffeine needs to find the amount and pattern of use that gives them alertness benefits without disrupting their sleep.”
_____________
Principal source: Krueger et al. (2011).
Additional information: Some studies have suggested that it is possible to drink coffee immediately before a nap. It takes about 20-30 minutes for the caffeine to become effective, so one can nap during that short period. Drivers may want to experiment with this approach.

## Slide 145: Two Harmful Stimulants
Amphetamines are illegal or available only with a prescription. Too strong for general use
  Increase activity level but do not improve performance reliably
  Increase heart rate and metabolism, sometimes dangerously
  Often you “crash” several hours after use
Nicotine does not improve alertness or performance. Smoking reduces oxygen flow to the brain
Notes: TtT Narration: “Two harmful stimulants: amphetamines and nicotine.”
__________
Additional comment: Use of illegal drugs like amphetamine is low among CMV drivers, in part due to drug testing. Smoking rates are very high, however, as discussed earlier.

## Slide 146: Sleep Aids: Supplements & Herbal Teas
Melatonin
  Natural hormone secreted every evening and related to sleep
  Small doses can facilitate nightly sleep
  Tablets tend to have much higher doses than needed
  No serious side effects known but has not been thoroughly tested
Valerian root
  Contains mixture of chemicals
  Sleep benefits reported
Supplements are not tested or regulated by the government
Notes: TtT Narration: “Melatonin and Valerian root are two herbal supplements used successfully by some people. Such supplements are not tested or regulated by the government, however.”
__________
Source: Krueger et al. (2011).
Additional information: Ramelteon (also called Rozerem) is a prescription drug which replicates the action of melatonin. Some studies suggest that it is safer for long-term use than hypnotic sleeping pills. Various other supplements and herbal teas (e.g. Chamomile, Kava Kava, Passion Flower). Benefits and safety not documented.

## Slide 147: Sleeping Pills (1 of 2)
Hypnotics = drugs used to induce sleep
Some also used to treat anxiety and stress disorders
General categories:
  Non-prescription Over-The-Counter (OTC); e.g., Tylenol PM, Benadryl
  Prescription:
    Benzodiazepines (e.g., Halcion, Restoril)
    Nonbenzodiazepines (e.g., Ambien, Sonota, Lunesta)
Notes: TtT Narration: “Over-the-counter and prescription sleeping pills can be helpful for sleeping, but they can also be harmful if used incorrectly. Following dosage directions is critical.”
____________
Additional information: A new prescription nonbenzodiazepine sleeping pill called Intermezzo is designed for those who wake up in the middle of the night and cannot get back to sleep. Its effects last about 4 hours. The same cautions about other sleeping medications apply.

## Slide 148: Sleeping Pills (2 of 2)
Cautions:
  No sleeping pill provides 100% natural sleep
  Most have side effects
  Most are habit-forming
  Some cause withdrawal symptoms
  Must allow full time for drug to leave your body before driving
Notes: TtT Narration: “Here are cautions in using sleeping pills.”
___________
Additional information: Recent research has suggested that use of sleeping pills can reduce overall longevity. Drivers should consider checking with their doctors and making efforts to reduce or stop sleeping pill use.

## Slide 149: Other Medications Have Fatigue Side Effects
Common side effects:
  Drowsiness
  Other fatigue
  Insomnia
Accordingly, many prescriptions specify when the drug should be taken (e.g., at bedtime)
Follow dosage instructions carefully
Safety regulations restrict driver on-road use of medications with stated fatigue side effects
Notes: TtT Narration: “Fatigue side-effects of other medications. You may want to initiate further discussion on U.S. and/or Canadian regulations on medication use, as well as any relevant company policies.”
_____________
Additional information: Fortunately, medication use per se is not known to be a major direct cause of crashes; but it can contribute to them. For example, most Benzodiazepines cause drowsiness, especially if combined with alcohol.

## Slide 150: Alcohol: Not a Sleep Medication
Not permitted in CMVs
Some drivers may use alcohol as a sleep aid at home.
Alcohol may make you sleepy, but it actually disrupts sleep:
  Disrupts REM (dream) sleep
  Causes “rebound” awakening after a few hours
Disruptive effects increase with age
Performance impairment effects greater when you are also sleepy
Alcohol makes OSA worse
Notes: TtT Narration: “Alcohol affects people differently. Its use in the hours before bedtime is usually disruptive to sleep.”
_________________
Additional information: Alcohol use by CMV drivers is rare as a primary cause of crashes.
Review question on drugs and medications: Q: The peak effects of caffeine occur about how long after drinking a cup of coffee? A: 60 to 90 minutes.”

## Slide 151: Lesson 4: Alertness & CMV Driving
Notes: TtT Narration: “Lesson 4 is Alertness and CMV Driving. Topics include Improving Sleep and Alertness, Scheduling and Hours-of-Service, and Team Driving.”

## Slide 152: Improving Sleep & Alertness
Topics:
Fatigue management challenges faced by CMV drivers
General strategies
At-home practices
On-road practices:
  General
  Night driving
  Dealing with shift and time zone changes
Notes: TtT Narration: “Here are the topics included in “Improving Sleep and Alertness.”
_____________
Additional instructor note:
Learning objectives for this section include:
(K) Recognize the various fatigue management challenges faced by CMV drivers
(K) Recognize positive strategies and practices (general, at-home, on-road).
(K) Recognize specific in-vehicle behaviors which do or do not promote alertness.
(K) Recognize fatigue-related concerns about night driving and shift changes.
(S) Apply fatigue management knowledge to successful night driving and/or shift changes.
(A) Value safety belt use (in part because of its importance in road departure crashes).

## Slide 153: Driver Fatigue Management Challenges (1 of 2)
Often a tight schedule for getting main sleep
Extended work hours (+ commuting for many)
Changing work schedules
Work/sleep periods conflict with circadian rhythms
Limited time for naps and other rest
Notes: TtT Narration: “This slide and the next one list ten different fatigue management challenges that CMV drivers may face. Not every item applies to every driver, but many drivers face most of these challenges in their jobs.”

## Slide 154: Driver Fatigue Management Challenges (2 of 2)
Unfamiliar or uncomfortable sleep locations
Disruptions of sleep
Limited opportunities for exercise
Difficulty in finding healthy foods on the road
Environmental stressors (e.g., noise, heat, cold, lack of ventilation)
Notes: TtT Narration: “The topic of driver fatigue management challenges is an excellent one for group discussion. You might ask drivers which of the challenges are greatest, or whether there are additional ones not listed here.”
______________
Additional instructor note: A follow-up question might focus on effective solutions to the biggest challenges.

## Slide 155: General Strategies to Meet These Challenges
SLEEP!!!
  Main sleep
  Naps
Maintain a healthful lifestyle
Try to keep a regular schedule
Go with your circadian rhythm – don’t fight it
Wind down before sleep
  Less physical activity
  Lower lights
Be smart about caffeine use
Notes: TtT Narration: “Here are six general strategies. Most have already been discussed in previous slides.”

## Slide 156: At-Home Strategies
Get the best sleep possible before starting a trip or work week
Communicate your sleep needs and get your family’s support
Bedroom should be:
  Completely dark
  Cool
  Quiet
Pre-sleep routine
Be active but don’t exhaust yourself. Take time to relax
Notes: TtT Narration: “Sleep hygiene starts at home. Here are some of the basics.”

## Slide 157: On-the-Road Strategies
Try to get as much sleep on the road as you get at home
Rest breaks with naps very beneficial
Also beneficial:
  Rest breaks without naps
  Moving your body
  Conversation if it is not distracting
Stimulation alone has little effect
Exercise
Avoid heavy meals
Wear your safety belt!
Notes: TtT Narration: “And drivers need to take their sleep hygiene practices on the road, where the challenges are much greater. On-road sleep hygiene and other fatigue management is another topic that students might want to discuss in class. Ask them what works for them. A related topic not addressed in the module is the relation of cab design and characteristics (e.g., noise) to fatigue. You might discuss this topic also.”
__________
Additional information on safety belt use: Many fatigue-related crashes are rollovers because CMVs leave the road and roll down embankments. Among major crash types, rollovers generally cause the most severe injuries for CMV drivers. Safety belts have their greatest benefits in CMV rollover crashes. Thus the importance of safety belt use! Source: Knipling, 2009.

## Slide 158: Night Driving
Advantage of night driving: less traffic!
Disadvantages:
  Fatigue, related to circadian rhythms
  More drunk/reckless motorists
  Poor visibility
Use light and dark to “fool” your body:
  Bright lights simulate daybreak
  Dark simulates night and bedtime
Use caffeine, but carefully
Consider taking sleeper berth period/nap in pre-dawn hours
Get more recovery sleep on weekends
Not for everybody!
Notes: TtT Narration: “Night driving is difficult from the fatigue management perspective. Drivers should appreciate both the advantage of night driving (less traffic) but also the disadvantages relating to fatigue and other factors. In particular, drivers need to develop strategies for dealing with the high-risk pre-dawn hours. As a discussion topic, you might ask drivers to share their ways of dealing with fatigue during overnight driving. Some carriers have specific policies relating to night driving; if your carrier has these, you should discuss them here.”
____________
Additional information: Opinions differ about the overall safety of night driving versus day driving. In regard to fatigue, however, there is no question that risk is greater during the overnight hours. In regard to the use of light to simulate daybreak, one should realize that the beneficial effects are not sufficient to overcome significant sleep loss. Bright lights help to keep you awake, but you cannot completely fool your body. Darkness, however, is almost always beneficial for improved sleep. Daytime sleepers should ensure that their sleeping quarters are completely dark.

## Slide 159: Dealing with Shift & Time Zone Changes
Be aware of your “body clock”
Short trips/shift changes: stick with your regular sleep schedule
Longer changes:
  “Pre-adjust” before change
  Shift your pre-bed, “evening” routine
  Use light and dark to help you adjust
  To stay awake, be physically active and interact with others
Getting more sleep generally makes changes easier
Notes: TtT Narration: “The topic of circadian rhythms was covered earlier under Factors Affecting Alertness and Performance. Shift and time zone changes involve circadian adjustments. This is another topic where drivers may want to share their personal experiences and fatigue management strategies. More information is presented later in the module on schedule rotations.”
___________
Optional check on learning: Q: Describe a good pre-sleep routine.
A: Wind down, relax, and perhaps lower the lights.

## Slide 160: Scheduling & Hours-of-Service
Topics:
Principles of sound scheduling
Schedule regularity; forward vs. backward rotations
Current HOS rules and their scientific rationales
Factors affecting your alertness and performance
Driver obligations
Notes: TtT Narration: “Here are the topics included in “Scheduling and Hours-of-Service.”
________
Additional instructor note:
Learning objectives for this section include:
(K) Recognize principles of sound scheduling; e.g., schedule regularity.
(K) Distinguish forward rotation from backward rotation, and relation to fatigue management.
(K) Identify key HOS rules and their relation to sleep hygiene.
(K) Recognize good and bad fatigue management work schedules (e.g., irregular, backward rotating).
(K) Recognize factors affecting driver alertness [including HOS compliance].
(A) Accept two driver obligations: HOS compliance and self-management “beyond compliance.”
Additional information: This instruction does not cover the details of HOS rules and students are not tested on their knowledge of specific rules (e.g., 10-hour rule, 14-hour rule, etc.). Instructors should avoid getting into detailed discussions about specific HOS rules; instead, focus on fatigue management principles.

## Slide 161: Basic Sleep-Rest Scheduling Practices
Regular schedule best
Strive for 7-8 hours sleep
Allow for commuting time
Allow for rest breaks and naps during work periods
Total time awake 16-17 hours per day or less
Work and rest cycle consistent with circadian rhythms when possible
Notes: TtT Narration: “This instruction does not focus on the details of HOS rules, and in the classroom you should avoid getting sidetracked discussing them. Instead, the emphasis is on basic scheduling practices, like those shown here.”

## Slide 162: Schedule Regularity
Stable, regular schedules best!
Schedule rotations: gradual better than abrupt
Schedule rotations: forward better than backward
Day 1
Day 2
Day 3
Notes: TtT Narration: “Here are a series of three slides showing a regular schedule, forward rotation, and backwards rotation.”

## Slide 163: Forward Schedule Rotation
Day 1
Day 2
Day 3
Notes: TtT Narration: “Forward schedule rotation. If your company has policies or practices relating to schedule rotations, now would be a good time to discuss them.”
_______________
Additional information: Traveling east to west results in a forward rotation of day- and nighttime hours, and thus is like a forward schedule rotation. Most people find this easier than going west to east.

## Slide 164: Backward Schedule Rotation
Day 1
Day 2
Day 3
Notes: TtT Narration: “Backward schedule rotation. There may be negative effects on the ability to sleep and the ability to stay awake while driving.”
___________
Additional information: Traveling west to east results in a backward rotation of day- and nighttime hours, and thus is like a backward schedule rotation. It often thrusts you into the next day before you have had sufficient sleep and while you are still in a circadian valley.

## Slide 165: U.S. Truck HOS Rules
HOS Element | Rule
Minimum total off-duty hours | 10 consecutive (prior to work shift)
Work shift and/or daily maximum driving hours | 11 (following 10 consecutive hours off-duty; during work shift driving window)
Work shift driving window (beyond which, no driving) | 14
Daily and work shift maximum on-duty hours (beyond which, no driving) | NA
Weekly maximum hours (beyond which, no driving) | 60 in 7 days 70 in 8 days
Restart | 34 consecutive hours
Split sleeper berth hours in 2 periods | 8+ (sleeper berth) and 2+ (off-duty and/or in sleeper berth)
Other | Time spent resting in parked CMV may be off-duty
Notes: TtT Narration: “Here are U.S. truck driver HOS rules. The table provides many details, but most details are not otherwise addressed in the instruction.”
___________
Additional comment: To the extent that specific HOS rules are discussed in your class, try to relate them to fatigue management principles rather than to compliance issues.

## Slide 166: U.S. Bus HOS Rules
HOS Element | Rule
Minimum total off-duty hours | 8 consecutive (prior to work shift)
Work shift and/or daily maximum driving hours | 10 (following 8 consecutive hours off-duty; during work shift)
Work shift driving window (beyond which, no driving) | NA
Daily and/or work shift maximum on-duty hours (beyond which, no driving) | 15 (work shift)
Weekly maximum hours (beyond which, no driving) | 60 in 7 days 70 in 8 days
Restart | NA
Split sleeper berth hours in 2 periods | 2+ and 2+ (sleeper berth, both periods); 8 total
Other | Time spent resting in parked CMV may be off-duty
Notes: TtT Narration: Here are the U.S. rules for bus drivers.

## Slide 167: Canadian Truck & Bus Rules
HOS Element | Rule
Minimum total off-duty hours | 10 (daily minimum); 8 consecutive (prior to work shift); 24 consecutive (within last 14 days)
Work shift and/or daily maximum driving hours | 13 (daily and work shift)
Work shift driving window (beyond which, no driving) | 16 consecutive after starting work shift
Daily and work shift maximum on-duty hours (beyond which, no driving) | 14 (daily and work shift)
Weekly maximum hours (beyond which, no driving) | 70 in 7 days (1) 120 in 14 days (2)
Restart | 36 consecutive hours (1) 72 consecutive hours (2)
Split sleeper berth hours in 2 periods | Single: 2+ and 2+ (sleeper berth, both periods), 10 total. Team: 4+ and 4+ (sleeper berth, both periods), 8 total. 10-hour total daily off-duty limit still applies
Other | Time spent resting in parked CMV may be off-duty
Notes: TtT Narration: “Canadian rules, shown here, are the same for truck and bus drivers.”

## Slide 168: HOS Rules
Relatively simple
Generally enforceable
Afford the opportunity for sufficient sleep and rest
“Level the playing field”
Help protect workers
Compliant carriers and drivers have lower crash rates
Notes: TtT Narration: “This slide summarizes the advantages HOS rules in relation to fatigue management. The intent is not to evaluate specific rules, but rather to show that HOS rules are necessary.”

## Slide 169
HOS Compliance
Amount of sleep
Circadian Rhythm
Time awake
Individual susceptibility
Task & Environmental factors
Self-awareness
Your Alertness and Performance
Notes: TtT Narration: “This slide recaps the many factors affecting alertness, starting with Hours-of-Service compliance.”
____________
Additional instructor note: “Self-awareness” is different from other factors in that it does not affect your fatigue level, but rather your ability to respond appropriately to fatigue. Most people do not have a precise awareness of their level of fatigue and likelihood of falling asleep.

## Slide 170: Driver Obligations
HOS rules are essential
You have two general safety obligations:
  (1) Comply with laws and regulations
  (2) Exercise good judgment beyond just complying with the rules
Similarly, you have two safety obligations relating to sleep and alertness:
  (1) Comply with HOS rules
  (2) Manage your fatigue and alertness beyond HOS compliance
Notes: TtT Narration: “The same two driver obligations apply to all aspects of safety: (1) comply with the rules; and (2) exercise good judgment beyond rule compliance.”
______________
Instructor Note: Check on Learning: Q: Which is generally best: a regular schedule, a forward-rotating schedule, or a backward-rotating schedule? A: regular schedule.; Q: Which is generally worst? A: A backward-rotating schedule.”

## Slide 171: Team Driving
Topics:
Advantages and disadvantages
Key U.S. and Canadian HOS sleeper berth rules
Compliant and safe sleeper berth use in team driving
Improving team driving
Notes: TtT Narration: “Here are the topics included in “Team driving.”
__________________
Additional instructor note:
Learning objectives for this section include:
(K) Identify key advantages and disadvantages of team driving.
(K) Recognize compliant and safe sleeper berth schedules.
(K) Identify general ways to improve team driving.

## Slide 172: Team Driving: Advantages
Drivers help each other stay awake
Drivers get more sleep
Drivers can rest when tired
Reduces time-on-task
Team drivers less likely to “push themselves to the limit”
Notes: TtT Narration: “Team driving advantages . . . “
___________________________
Additional information: Advantages and disadvantages based primarily on naturalistic driving study of team and solo drivers (Dingus et al., 2002). Also reviewed in Knipling (2006) and Knipling (2009).

## Slide 173: Team Driving: Disadvantages
Poorer quality sleep in moving vehicles
Greater use of split sleep may disrupt sleep patterns
Can mean shorter rest breaks when vehicle is stopped
Can mean greater fatigue at beginning of trip
Notes: TtT Narration: “and some disadvantages, both based on safety research.”
___________________
Additional information: Advantages and disadvantages based primarily on naturalistic driving study of team and solo drivers (Dingus et al., 2002). Also reviewed in Knipling (2006) and Knipling (2009).

## Slide 174: Key U.S. Sleeper Berth Rules
Trucks: Drivers using the sleeper berth provision must take at least 8 consecutive hours in the sleeper berth, plus a separate 2 consecutive hours either in the sleeper berth, off duty, or any combination of the two. | Buses: Drivers using a sleeper berth must take at least 8 hours in the sleeper berth, and may split the sleeper-berth time into two periods provided neither is less than 2 hours.
Notes: TtT Narration: “Here are key U.S. sleeper berth rules for truck and for bus drivers.”

## Slide 175: Key Canadian Sleeper Berth Rules
Single Drivers (Truck or Bus): Single drivers may split their 10 hours off-duty in no more than 2 periods provided that: (a) neither period in the sleeper berth is shorter than 2 hours; (b) the total of the 2 periods in the sleeper berth is at least 10 hours. | Team Drivers (Truck or Bus): Team drivers may split their 10 hours off-duty by spending 2 periods in the sleeper berth to obtain at least 8 or those hours, provided that: (a) neither period in the sleeper berth is shorter than 4 hours; (b) the total of the 2 periods in the sleeper berth is at least 8 hours.
Notes: TtT Narration: “In Canada, the rules are the same for truck and bus drivers, but different for single and team drivers.”

## Slide 176: Compliant & Safe Sleeper Berth Use
Plan sleeper berth periods in advance to be compliant and beneficial
When possible, take sleep periods during circadian valleys
Avoid both caffeine and strenuous activity in hours before breaks
Keep sleeper berth totally dark or use eyeshades
Don’t drive immediately after awakening
Notes: TtT Narration: “Here are five tips for compliant and safe sleeper berth use.”
________________
Additional information: Some drivers like to use a sound machine or fan in the sleeper berth to mask road noise. In regard to circadian valleys: Ordinarily both drivers will not be able to sleep during these periods. Nevertheless, the team should work to ensure that one driver takes advantage of these periods. If a stop is planned where both drivers can sleep, circadian valleys are the best times (especially 2 to 7am).

## Slide 177: Improving Team Driving
Team driving is a partnership!
To sleep well, each driver must have full confidence in the other driver
Driver should strive to be “smooth operator”
Agree on a game plan for sleep and rest that meets each driver’s needs
Notes: TtT Narration: “And, finally, here are some more general suggestions for improving team driving.”
___________
Instructor Note: Review question on team driving. Q: We cited five advantages of team driving for alertness. Can you state three of them?
A: Any three of these:
Drivers help each other stay awake.
Drivers get more sleep
Drivers can rest when tired
Reduces time-on-task
Team drivers less likely to push themselves to the limit.”

## Slide 178: Conclusion: Review and Summary
Notes: TtT Narration: “Here is the Module conclusion, including a review and summary of key points.”

## Slide 179: Review
Topics:
Key terms and concepts
Myths (misconceptions) about sleep and alertness
Recap of fatigue management “Dos” and “Don’ts”
Notes: TtT Narration: “Here is what will be reviewed.”

## Slide 180: Review: Key Fatigue Terms & Concepts (1 of 2)
Sleep hygiene
Subjective vs. objective self-assessment
Microsleeps
“Drift and jerk” steering
Sleep debts and recovery
Sleep structure (e.g., Non-REM vs. REM)
Notes: TtT Narration: “Here is the first of two slides reviewing key module terminology and concepts.”
__________
Additional instructor note: Consider going through the list, asking who can define the term and/or explain it. Most can be described briefly and concisely. As instructor, you should be prepared to explain any items or correct any misunderstandings.

## Slide 181: Review: Key Fatigue Terms & Concepts (2 of 2)
Internal vs. task-related fatigue
Circadian rhythms
Time awake
Time-on-task
Individual differences in fatigue susceptibility
Sleep disorders (OSA, insomnia)
Forward vs. backward schedule rotation
Notes: TtT Narration: “Here is the second of two review slides.”
___________
Additional instructor note: Consider going through the list, asking who can define the term and/or explain it. Most can be described briefly and concisely. As instructor, you should be prepared to explain any items or correct any misunderstandings.

## Slide 182: Fatigue Myths (1 of 2)
“I can discipline myself to get by with less sleep”
“I can motivate myself to push through even though I’m sleepy”
“I’ve lost sleep before and done just fine”
“I know how sleepy I am”
Notes: TtT Narration: “Here is the first of two slides presenting fatigue myths. The slide narration explains why these statements are incorrect. Can you explain them?”
_______________
Additional instructor note: As instructor, you should be prepared to explain any items or correct any misunderstandings.

## Slide 183: Fatigue Myths (2 of 2)
“I can always just open the windows and turn up the radio”
“A nap will only make it worse”
“Alcohol helps me sleep”
“Dealing with driver fatigue is easy”
Notes: TtT Narration: “Here is the second of two slides on fatigue myths.”
__________
Additional instructor note: As instructor, you should be prepared to explain any items or correct any misunderstandings.

## Slide 184: Fatigue Management “Do’s” (1 of 2)
Value alertness and wellness
Recognize sleep as a main ingredient
Be aware of the fatigue factors affecting you at any time
Self-assess your fatigue level based on objective signs
Try to “go with” your circadian rhythms, not against them
Use dark and light as aids to fatigue management
Notes: TtT Narration: “Finally, there are two slides on fatigue management “Do’s” and one on “Don’ts. Can you explain them?”
____________
Additional instructor note: As with the previous slides, consider going through the list, asking students if they can explain each item. Or you might just select a few of them for discussion. As instructor, you should be prepared to explain any items or correct any misunderstandings. Examples: What are the fatigue factors affecting you at any time? How can you use darkness as an aid to fatigue management? How can you use light?

## Slide 185: Fatigue Management “Do’s” (2 of 2)
Seek OSA screening if you have risk factors
Follow the 5 keys to wellness
Use caffeine wisely
Be cautious about other drugs
Take breaks, especially with naps
Comply with HOS rules
Wear your safety belt!
Notes: TtT Narration: “Here is the second slide on “Do’s. Why is safety belt use a part of fatigue management? Because fatigue-related crashes are usually run-off-road or rollovers, the crashes where you need your safety belt the most.”
_______________
Additional instructor note: As with the previous slides, consider going through the list, asking students if they can explain each item. Or you might just select a few of them for discussion. As instructor, you should be prepared to explain any items or correct any misunderstandings. Examples: Can you name the five keys to wellness (Optional hint: The first was nutrition)? Why is a nap better than a break without a nap?

## Slide 186: Fatigue Management “Don’ts”
Ignore signs of fatigue
Use caffeine excessively
Use alcohol as a sleep aid
Eat heavy meals before driving
Rotate your daily work-rest schedule backwards (when you can avoid it)
Exercise strenuously just before sleep periods
Let a sleep debt worsen
Set the alarm clock on weekends
Notes: TtT Narration: “Here are some fatigue management Don’ts. We can’t always manage our lives perfectly, but we can try to do better!”
____________
Additional instructor note: As with the previous slides, consider going through the list, asking students if they can explain each item. Or you might just select a few of them for discussion. As instructor, you should be prepared to explain any items or correct any misunderstandings. Examples: Why is alcohol bad for sleep? Why is it better to not set the alarm on weekends?

## Slide 187: Quiz - Driver Education Review: Part 2
One survey of CMV drivers found that their biggest expressed concern was:
  Difficulty finding healthy foods on the road
  Excessive physical exertion
  Wanting to stop smoking
  Lack of sufficient family time.
Notes: Correct Answer: D

## Slide 188: Quiz - Driver Education Review: Part 2
Which is likely to be least effective as a short-term fatigue countermeasure while on a trip?
  Sipping coffee
  Turning on cruise control and moving feet
  Turning up the radio
  Taking a nap.
Notes: Correct Answer: C

## Slide 189: Quiz - Driver Education Review: Part 2
Which is true of HOS rules?
  HOS rule compliance ensures driver alertness
  HOS rules provide for driver individual differences
  HOS rules provide unlimited flexibility
  HOS violation rates are related to driver and carrier crash rates.
Notes: Correct Answer: D

## Slide 190: Quiz - Driver Education Review: Part 2
Which sequence best rank orders these three general schedule patterns from best to worst?
  Forward-rotating, backward-rotating, regular
  Forward-rotating, regular, backward-rotating
  Backward-rotating, regular, forward-rotating
  Regular, forward-rotating, backward-rotating.
Notes: Correct Answer: D

## Slide 191: Quiz - Driver Education Review: Part 2
Which is NOT good sleep hygiene advice?
  On weekends, set your alarm clock for the same time as you set it during the work week
  Focus on objective signs of fatigue, not subjective ones, while driving
  Use dark to help you feel sleepy and light to help keep you awake
  Use caffeine to help sustain alertness, but not excessively or too close to sleep periods.
Notes: Correct Answer: A

## Slide 192: Family Education Training & Behavior Change
Notes: Complete Narration: “This train-the-trainer lesson covers Module 4, the family education training, as well as the topic of fatigue management behavior change.”

## Slide 193: Family Education Training
Topics:
Module 4 purpose and features
Learning goals and objectives
Conducting Module 4 training
Notes: Complete Narration: “In our review of the family education training, we will review Module 4’s purpose and features, its learning goals and objectives, and conducting Module 4 training. Since Module 4 is largely a subset of Module 3, we will not review the individual slides. You should review them yourself if you are unsure of the material.”
____________
Additional instructor note:
Section learning objectives (Note: Some of these are acquired through learning and review of Module 3, which covers almost all of the Module 4 material, often in greater depth.):
(K) Recognize key features of Family Education module.
(K) Identify training facilities, equipment, and materials needed.
(K) Identify record-keeping requirements (less than in Module 3).
(K/S/A) Attain all Module 4 learning objectives at a higher level than in original instruction (i.e., presentation will be at higher level and test items will be more challenging).
(K) Identify appropriate discussion topics and other training methods applicable to Module 4 sections.
(K) Identify methods to organize company events to include presentation of Family Education module.
(S) Be able to effectively teach Module 4 in family group settings.

## Slide 194: Module 4 (Family Education) Purpose & Features
Target audience: driver spouses & families
Duration: ~45 minutes
Organization: Introduction, 3 Lessons, Conclusion
Instructional modes:
  Instructor-led PowerPoint (with instructor notes)
  Web-based
Informal testing:
  Checks on learning at end of most sections
  Optional 10-item exam
Notes: Complete Narration: “The target audience for Module 4 is driver spouses and families. Driver families can play a major, positive role in driver health and safety. Module 4 lasts about 45 minutes. It consists of an Introduction, three short lessons, and a Conclusion. Like other modules, it can be instructor-led with PowerPoint slides, or it can be taken online. Module 4 testing is informal and simply to reinforce learning. There are checks on learning at the end of most sections, and there is an optional 10-item exam at the end.”

## Slide 195: Module 4 Learning Goals
(K) Recognize the major facts, concepts, procedures, and principles of fatigue, alertness, sleep, & wellness.
(S) Apply this knowledge to lifestyle and behavior at home.
(A) Value sleep & wellness as major factors in performance, safety, & happiness for the driver and for the whole family.
Notes: Complete Narration: “Module 4’s KSAs are a subset of those for Module 3, but with emphasis on home and family. Lifestyle changes are most likely to be significant and long-lasting if they involve the whole family, not just the driver.”
__________
Additional instructor note: As in Module 3, most of the Module 4 training is directed toward knowledge goals, with the assumption that increased knowledge will be reflected in attitude and behavior change.

## Slide 196: Module 4 Lessons & Topics
Introduction
Fatigue Basics
Alertness, Sleep, Wellness, & Performance
What is Fatigue?
Fatigue Characteristics
Fatigue-Related Crashes
Physiology of Sleep & Alertness
What is Sleep?
Factors Affecting Alertness & Fatigue
Sleep Disorders
Health & Alertness
Health & Wellness
Drugs & Medications
Improving Sleep & Alertness
Conclusion
Notes: Complete Narration: “As a reminder, here are the lessons and topics of Module 4, Family Education. They are also a subset of those in Module 3. Take a moment to review them . . . “

## Slide 197: Conducting Module 4 Training
Spouses and families should be invited, not required, to take the training
Consider holding a family-oriented event when the PowerPoint is presented
Driver families may also access web-based module
Family Education checks on learning and exam are intended to be easy and fun, not threatening
Notes: Complete Narration: “The approach to conducting Module 4 is quite different than that for Module 3. Spouses and families should be invited, not required, to take the training. Consider holding a family-oriented event (such as a dinner or cookout) when the PowerPoint is presented. Driver families may also log onto the web-based module from their home computers. You should provide drivers with information on how they can access the web-based training from their homes, and help with any access problems. The Family Education checks on learning and exam are intended to be easy and fun, not threatening.”
_________________________
Additional instructor note: Approaches to providing the Module 4 training will vary from company to company. Each NAFMP company should have a specific plan for it, however. One effective combination is likely to be a family-oriented event with the classroom training, plus provision of at-home access to the web-based version as an alternative.

## Slide 198: Facilitating Behavior Change
Topics:
Carrier management role
Keys to driver sleep hygiene improvements
Behavior change process
Behavioral self-management
SMART goal-setting
Notes: Complete Narration: “Our final topic is facilitating behavior change. Ultimately, that is your most important role as an FMP trainer. We’ll be talking about the carrier management role in driver behavior change, keys to driver sleep hygiene improvements, the behavior change process, behavioral self-management, and “SMART” goal-setting.”
___________
Additional instructor note:
Section learning objectives:
(K/A) Know and accept carrier and trainer role in facilitating driver (and family) behavior change.
(K) Identify keys to driver sleep hygiene improvements
(K) Recognize five stages in the behavior change process, their sequence, and associated goals and strategies for each stage.
(K) Recognize four elements in behavioral self-management.
(K) Recognize the five elements of SMART goal-setting.

## Slide 199: Carrier Role in Facilitating Driver & Family Behavior Change
Establish safety culture
Set good example
Assess needs
Develop a plan
Implement program in supportive environment
Key FMP elements:
  Training
  Medical screening
  Alertness-friendly scheduling/dispatching
  Individualized support for drivers
Evaluate and improve program
Notes: Complete Narration: “When a carrier chooses to adopt an FMP, it also accepts certain roles in facilitating driver and family behavior change. Carrier management should establish a safety culture and set a good example for drivers. Carrier management should assess needs and develop a plan for driver fatigue reduction and health improvement. It should implement the program in a supportive environment, including both the operational and social environments of the company. Key FMP elements include training, medical screening, “alertness-friendly” scheduling and dispatching, and individualized support for drivers. Finally, a carrier should continually evaluate and improve the program.”
___________
Additional instructor note: See the NAFMP Implementation Guide for more information and resources relating to the carrier role in the NAFMP.

## Slide 200: Keys to Driver Sleep Hygiene Improvements
Knowledge/awareness
Overcome ambivalence
Target specific behaviors
Core healthful behaviors; e.g.,
  Exercise
  “Strive for five” fruits and vegetables daily
  Napping
Specific goals
Social support
Notes: Complete Narration: “Here are some keys to driver sleep hygiene improvements. First is knowledge and awareness, both of the negative effects of current behaviors and the positive effects of change. Drivers next need to overcome ambivalence – to get off the fence and commit to change. They should target specific healthful behaviors. Core healthful behaviors are those that help lead to other behavioral improvements. Exercise, eating more fruits and vegetables, and napping are three such core behaviors. As drivers begin to change, they should set specific goals. Social support from family and co-workers helps to reinforce improvements.”
_________________
Additional instructor note: As noted in Module 3 and elsewhere, the terms “sleep hygiene” and “fatigue management” are largely synonymous. The next slide will begin a series on steps in behavior change. Before beginning that, consider asking your trainees whether they have changed any specific health- or safety-related behaviors over the past few years, and whether they would want to discuss their process and experience in making the change. Increasing exercise and improving diet are always good examples. If the example is weight loss, the focus of the discussion should be on behaviors, not weight loss per se.

## Slide 201: Steps to Behavior Change
Aware, thinking
of change
Unaware
of
problem
Taking action
Planning
to change
Sustaining action
Health, Wellness, Alertness, Performance
Notes: Complete Narration: “Research on behavior change has suggested that people go through five steps or stages along the way toward better behavioral health. Specifics of the process will vary for different people and different behaviors. But there are usually five steps. At first, a person is unaware of their problem (or perhaps just unwilling to think about it!). Before change can even begin, they have to become aware of the problem and start thinking about changing. Thinking becomes planning, and next becomes action. Just taking action is not enough since it is always easy to slip back. The final step is sustaining action and enjoying the benefits. Benefits include health, wellness, alertness, and better performance.”
_________________
Additional instructor note: Review question: Q: Why did we call certain types of healthful behaviors like exercise core behaviors?
A: Because people who exercise tend to also adopt other healthful behaviors also.

## Slide 202: Stages of Behavior Change
Stage | Thinking & Behavior
1. Pre-Contemplation | Unaware or unaccepting of problem; no thoughts of change
2. Contemplation | Aware of problem and thinking about change
3. Preparation | Plan to change
4. Action | Making specific behavior changes
5. Maintenance | Sustaining desirable actions
Notes: Complete Narration: “Researchers have defined and analyzed the five steps we just saw. Here are the same five steps, described in more detail as stages of behavior change. During the first or Pre-Contemplation stage, a person is unaware or unaccepting of their problem, and has no thoughts of change. A breakthrough occurs in the Contemplation stage when a person becomes aware of the problem and thinks about change. Next, in the Preparation stage, a person plans to change. In the Action stage, a person makes specific behavior changes; for example, they actually exercise aerobically for two and a half hours during a week as suggested by health experts. In the final stage, Maintenance, actions are sustained. The person exercises for two and a half hours every week, or at least most weeks.”
____________
Additional instructor Note: These five stages of behavior change are from the Transtheoretical Model developed by Prochaska et al. (1992). Summaries are contained in Roberts and York (2000) and Simons-Morton et al. (2012). Both of these publications also present other theories, models, and concepts of behavior change. Since trainers are supposed to be mentors for behavior change as well, they should know this sequence of behavior change and key features of each stage.

## Slide 203: Behavior Change: Stages of Thought About Reducing Fat Consumption
Stage | Thoughts About Reducing Fat Consumption
1. Pre-Contemplation | “I enjoy double cheeseburgers and fries. I have no intention of eating lower-fat foods.”
2. Contemplation | 
3. Preparation | 
4. Action | 
5. Maintenance | 
Notes: Complete Narration: “A person’s thinking also changes as they go through the stages of behavior change. Let’s consider one’s thoughts about reducing fat consumption. During the pre-contemplation stage, a person is not thinking about the problem. They might say to themselves, ‘I enjoy double cheeseburgers and fries. I have no intention of eating lower-fat foods.’”
_______________
Additional instructor note: Adapted from presentation in Roberts and York (2000), based on Greene et al. (1994). Exercise equivalent: “Exercise is too much like work. I want to relax and enjoy life.”

## Slide 204: Behavior Change: Stages of Thought About Reducing Fat Consumption
Stage | Thoughts About Reducing Fat Consumption
1. Pre-Contemplation | “I enjoy double cheeseburgers and fries. I have no intention of eating lower-fat foods.”
2. Contemplation | “Maybe I could try a chicken sandwich instead – if it tastes good and doesn’t cost too much.”
3. Preparation | 
4. Action | 
5. Maintenance | 
Notes: Complete Narration: “But, beginning with the Contemplation stage, they begin to think about the problem. ‘Maybe I could try a chicken sandwich instead – if it tastes good and doesn’t cost too much.’”
_______________
Additional instructor note: Adapted from presentation in Roberts and York (2000), based on Greene et al. (1994). Exercise equivalent: “Maybe I should exercise more, but I don’t know where to start.”

## Slide 205: Behavior Change: Stages of Thought About Reducing Fat Consumption
Stage | Thoughts About Reducing Fat Consumption
1. Pre-Contemplation | “I enjoy double cheeseburgers and fries. I have no intention of eating lower-fat foods.”
2. Contemplation | “Maybe I could try a chicken sandwich instead – if it tastes good and doesn’t cost too much.”
3. Preparation | “I’ll try to eat lower-fat foods when I can. I’d like to do more, but I’m not sure how.”
4. Action | 
5. Maintenance | 
Notes: Complete Narration: “During the Preparation stage they start planning to change. They may say to themselves and others, ‘I’ll try to eat lower-fat foods when I can. I’d like to do more, but I’m not sure how.”
____________________
Additional instructor note: Adapted from presentation in Roberts and York (2000), based on Greene et al. (1994). Exercise equivalent: “I’ll at least try to walk more. Maybe just 10 minutes each morning before I start to drive.”

## Slide 206: Behavior Change: Stages of Thought About Reducing Fat Consumption
Stage | Thoughts About Reducing Fat Consumption
1. Pre-Contemplation | “I enjoy double cheeseburgers and fries. I have no intention of eating lower-fat foods.”
2. Contemplation | “Maybe I could try a chicken sandwich instead – if it tastes good and doesn’t cost too much.”
3. Preparation | “I’ll try to eat lower-fat foods when I can. I’d like to do more, but I’m not sure how.”
4. Action | “I’m eating lower-fat foods by not stopping at fast food restaurants and by making better food choices. But it’s sometimes hard when I’m on the road.”
5. Maintenance | 
Notes: Complete Narration: “In the Action stage, behavior has changed. In regard to fat consumption, they may say, ‘I’m eating lower-fat foods by not stopping at fast food restaurants and by making better food choices. But it’s sometimes hard when I’m on the road.’”
_______________
Additional instructor note: Adapted from presentation in Roberts and York (2000), based on Greene et al. (1994). Exercise equivalent: “I take a walk most mornings before driving, but it’s hard to exercise much more than that.”

## Slide 207: Behavior Change: Stages of Thought About Reducing Fat Consumption
Stage | Thoughts About Reducing Fat Consumption
1. Pre-Contemplation | “I enjoy double cheeseburgers and fries. I have no intention of eating lower-fat foods.”
2. Contemplation | “Maybe I could try a chicken sandwich instead – if it tastes good and doesn’t cost too much.”
3. Preparation | “I’ll try to eat lower-fat foods when I can. I’d like to do more, but I’m not sure how.”
4. Action | “I’m eating lower-fat foods by not stopping at fast food restaurants and by making better food choices. But it’s sometimes hard when I’m on the road.”
5. Maintenance | “I’m following my low-fat food plan and feel great. I’m proud of my weight loss and knowing that I’ve improved my health.”
Notes: Complete Narration: “In the Maintenance stage, people are proud but also determined to retain their gains. You might hear them say, ‘I’m following my low-fat food plan and feel great. I’m proud of my weight loss and knowing that I’ve improved my health.’”
__________
Additional instructor note: Adapted from presentation in Roberts and York (2000), based on Greene et al. (1994). Exercise equivalent: “I almost always take two walks a day, and on weekends I lift weights and go for a longer walk with my wife and our dogs.”

## Slide 208: Behavior Change: Stages of Thought About Reducing Fat Consumption
Stage | Thoughts About Reducing Fat Consumption
1. Pre-Contemplation | “I enjoy double cheeseburgers and fries. I have no intention of eating lower-fat foods.”
2. Contemplation | “Maybe I could try a chicken sandwich instead – if it tastes good and doesn’t cost too much.”
3. Preparation | “I’ll try to eat lower-fat foods when I can. I’d like to do more, but I’m not sure how.”
4. Action | “I’m eating lower-fat foods by not stopping at fast food restaurants and by making better food choices. But it’s sometimes hard when I’m on the road.”
5. Maintenance | “I’m following my low-fat food plan and feel great. I’m proud of my weight loss and knowing that I’ve improved my health.”
Notes: Complete Narration: “Take a moment to look back over the five stages and typical thoughts during each. Can you see any parallels to your own thoughts about a behavior you have changed? What about your co-workers and family members? Next we’ll talk about goals and strategies for helping people to move through these stages.”
_________________
Additional instructor note: Adapted from presentation in Roberts and York (2000), based on Greene et al. (1994). The equivalent statements about exercise on previous notes pages could be used to quiz trainees on their understanding.

## Slide 209: Behavior Change Goals & Strategies
Stage | Goal | Strategies
1. Pre-Contemplation | Personalize risks | Increase knowledge/awareness of negative outcomes. Discuss personal effects of current behavior. Create a supportive environment for improvement.
2. Contemplation |  | 
3. Preparation |  | 
4. Action |  | 
5. Maintenance |  | 
Notes: Complete Narration: “Let’s go through the same sequence, but this time looking at goals and strategies for behavior change during each stage. During the Pre-Contemplation Stage, a person is unaware (or perhaps doesn’t want to be aware) of the problem. A communication goal is to personalize risks so a driver sees the problem in a personal light. Specific strategies include:
Increase knowledge and awareness of negative outcomes.
Discuss personal effects of the driver’s current behavior, and
Create a supportive environment for improvement.”
_______________
Additional instructor note: Adapted from presentation in Roberts and York (2000). The goals and strategies in each of the first four stages are to help the person enter into the next stage. Much of the information presented in the Health & Wellness sections of Modules 3 and 4 is intended to “personalize risks” relating to poor nutrition, lack of exercise, smoking, and other negative behaviors.

## Slide 210: Behavior Change Goals & Strategies
Stage | Goal | Strategies
1. Pre-Contemplation | Personalize risks | 
2. Contemplation | Increase self-confidence | Identify problem behaviors and barriers to change. Prioritize behaviors. Encourage development of a plan and goals. Enlist support from family and friends.
3. Preparation |  | 
4. Action |  | 
5. Maintenance |  | 
Notes: Complete Narration: “Now that the person is thinking about their problem, we have to increase their self-confidence to change. Try to:
Help them identify their problem behaviors and barriers to change.
Help them prioritize behaviors.
Encourage development of a plan and goals, and
Enlist support from family and friends.
A main purpose of Module 4 is to enlist this support.”
_______________
Additional instructor note: Adapted from presentation in Roberts and York (2000). The goals and strategies in each of the first four stages are to help the person enter into the next stage. Discussion question: What would be your priority behavior for change? What do you think your company drivers would say? Exercise more? Stop smoking? Note: For this and other questions involving personal behavior and medical conditions, do not pry into any individual’s personal situation. Many people like to talk about these things, but many others do not.

## Slide 211: Behavior Change Goals & Strategies
Stage | Goal | Strategies
1. Pre-Contemplation | Personalize risks | 
2. Contemplation | Increase self-confidence | 
3. Preparation | Initiate change | Encourage small initial steps and gradual goals. Discuss earlier attempts and ways to succeed this time. Help them develop concrete plans.
4. Action |  | 
5. Maintenance |  | 
Notes: Complete Narration: “Now our driver is preparing to change. We have to help make it happen.
Encourage small initial steps and gradual goals.
Discuss earlier attempts and ways to succeed this time.
Help them develop concrete action plans.”
___________
Additional instructor note: Adapted from presentation in Roberts and York (2000). The goals and strategies in each of the first four stages are to help the person enter into the next stage. Discussion question: Select an area of health behavior (nutrition, exercise, etc.) and discuss appropriate “small initial steps and gradual goals.

## Slide 212: Behavior Change Goals & Strategies
Stage | Goal | Strategies
1. Pre-Contemplation | Personalize risks | 
2. Contemplation | Increase self-confidence | 
3. Preparation | Initiate change | 
4. Action | Commit to change | Provide feedback; reinforce positive changes. Provide problem-solving advice. Encourage self-rewards and celebrations of success.
5. Maintenance |  | 
Notes: Complete Narration: “In the Action Stage, a person’s behavior has changed, but they need to commit to that change.
Provide feedback and reinforce positive changes.
Provide problem-solving advice.
Encourage self-rewards and celebrations of success.”
____________
Additional instructor note: Adapted from presentation in Roberts and York (2000). The goals and strategies in each of the first four stages are to help the person enter into the next stage. Discussion question: What are the most important rewards of positive behavior change? In other words, what are the strongest reinforcers? Feeling better? Looking better? Sense of accomplishment?

## Slide 213: Behavior Change Goals & Strategies
Stage | Goal | Strategies
1. Pre-Contemplation | Personalize risks | 
2. Contemplation | Increase self-confidence | 
3. Preparation | Initiate change | 
4. Action | Commit to change | 
5. Maintenance | Continue commitment | Reinforce lifestyle changes and benefits. Discuss importance of maintaining change. Discuss ways to deal with relapses.
Notes: Complete Narration: “In the first four stages, we were trying to help the driver progress to the next phase. Now he or she has arrived! We are trying to help them continue their commitment and keep their gains. As a behavior change agent, you should:
Reinforce their lifestyle changes and their benefits.
Discuss the importance of maintaining change, and
Discuss ways to deal with any relapses.”
______________
Additional instructor note: Adapted from presentation in Roberts and York (2000). “Maintenance” is the final stage. Discussion question: Thinking of your own past positive behavior changes, which ones have you been able to maintain? Which ones have you not maintained? What has been the difference?

## Slide 214: Behavior Change Goals & Strategies
Stage | Goal
1. Pre-Contemplation | Personalize risk
2. Contemplation | Increase self-confidence
3. Preparation | Initiate change
4. Action | Commit to change
5. Maintenance | Continue commitment
Notes: Complete Narration: “Take a minute to review the stages of behavior change and their goals. Try to use them in your interactions with drivers and other students. As you talk to students, try to be aware of their stage of behavior change and target your suggestions accordingly.”
_________________
Additional instructor note: Adapted from presentation in Roberts and York (2000). The goals and strategies in each of the first four stages are to help the person enter into the next stage.

## Slide 215: Behavioral Self-Management Helps Good Performers to Become Even Better!
Objective self- measurement of performance
Goal-setting for improvement
Self-monitoring to review progress
Self-rewards for success
Notes: Complete Narration: “People in the “Action” and “Maintenance” stages of behavior change might adopt Behavioral Self-Management. It helps good performers to become even better. The figure presents a personal example – increasing exercise. Behavioral self-management begins with objective measurement of performance. In our example, exercise is measured in minutes. Next, set simple daily or weekly goals. Self-monitor progress in achieving those goals. Tangible self-rewards for success help to reinforce behavior change, although many adults find the personal satisfaction of goal achievement to be the main reward.”
___________
Additional instructor note: Graphic from Safety for the Long Haul; Large Truck Crash Risk, Causation, & Prevention (Knipling, 2009). Used with permission. Systematic behavioral self-management probably works best for people who already have a good base of health-related behaviors. For those just starting, it is probably best to focus on just one or two elements, such as objective self-measurement of performance (example: writing down daily minutes of exercise on a calendar).

## Slide 216: SMART Goal Setting
Specific behaviors targeted
Motivationally effective
Attainable (challenging but achievable)
Relevant to drivers’ lives, performance, & safety
Trackable (can be measured and recorded)
Notes: Complete Narration: “Whether we are talking about drivers, other people, or organizations, goal-setting should be smart. “SMART” is an acronym which captures five elements of successful goal-setting. In smart goal-setting, specific behaviors are targeted. “Walking” and “eating fruits and vegetables” are two good examples. Next, goals should be motivationally effective – in other words, something that is important to you. Goals must be attainable, especially in the early stages. That is, they should be challenging but achievable. Next, goals should be relevant to drivers’ lives, performance, and safety. Objectively, diet, exercise, and sleep are all very relevant to a driver’s life, but it’s important that he or she sees the relevance. Finally, goals should be trackable or measurable. Walking could be measured in two different ways – time and distance. “Minutes of walking” is probably the easiest measure. Anything measured can be recorded. If drivers keep a calendar and record their minutes of walking every day, they will be much more likely to sustain their behavior change.”
__________
Additional instructor note: Source: Geller (2001). Discussion question: Can you think of any past personal or organizational goals that have been “SMART.” Any that were not “SMART?” What were the outcomes?

## Slide 217: Quiz - Family Education & Behavior Change
If a person is in the ___________ stage of behavior change, you should help them begin change with small initial steps and goals.
  Pre-Contemplation
  Contemplation
  Preparation
  Action
  Maintenance.

## Slide 218: Quiz - Family Education & Behavior Change
When a person is in the _________ stage, he or she is aware of their health problem, and thinking about changing. As a change agent, you should try to increase their self-confidence and identify problem behaviors and barriers to change.
  Pre-Contemplation
  Contemplation
  Preparation
  Action
  Maintenance.

## Slide 219: Quiz - Family Education & Behavior Change
Of the following, which is probably least essential for effective self-management (e.g., of exercise, diet, other health-related behaviors)?
  Objective measurement of performance
  Goal-setting
  Self-monitoring to review progress
  Financial rewards.

## Slide 220: Quiz - Family Education & Behavior Change
Which element of SMART goal-setting is incorrectly stated?
  Social
  Motivationally effective
  Attainable
  Relevant
  Trackable.

## Slide 221: Quiz - Family Education & Behavior Change
Which is NOT a typical characteristic of adult learners?
  Self-directed
  Like to know why they need to learn
  Prefer an environment of mutual trust and respect
  Learn from experience
  Prefer passive to active involvement.

## Slide 222: Conclusion: Review and Summary
Notes: Complete Narration: “Congratulations! You’ve come a long way. You have successfully completed Modules 3 and 4, and are on the verge of completing Module 5, Train-the-Trainer. We’ll review some key concepts and then take the module exam.”

## Slide 223: The Challenges of FMP Training (1 of 2)
Becoming an expert on driver fatigue, alertness, wellness, & performance
Being a role model
Understanding FMP structure & purpose
Developing your classroom skills
  Presentation
  Student interaction
  Maintaining standards & accountability
Notes: Complete Narration: “As you probably already realize, there are many challenges in being a successful FMP trainer. There is the challenge of becoming an expert on driver fatigue, alertness, wellness, and performance. You need to be a role model. You need to understand the FMP structure and purpose. There is also the challenge of developing your classroom skills, including skills for presentations, student interaction, and maintaining standards and accountability.”
_____________
Additional instructor note: Most of these items correspond to module KSAs presented earlier.

## Slide 224: The Challenges of FMP Training (2 of 2)
Becoming a facilitator for web-based training
  Coordination & planning
  Computer skills
  Monitoring progress
  Problem-solving
Being an agent of positive change in people’s lives.
Saving lives!
Notes: Complete Narration: “Further challenges include those of becoming a facilitator for the web-based training. This includes coordination and planning, computer skills, monitoring student progress, and problem-solving. Finally, there are the challenges of being an agent of positive change in people’s lives and, ultimately, saving lives!”
___________
Additional instructor note: Discussion question: Which aspect(s) of being an NAFMP trainer do you consider to be most difficult? Which will likely be the easiest?

## Slide 225: Review: Key Training-Related Terms & Concepts
Classroom training
Web-based training
Learning goals & objectives
KSAs
Characteristics of adult learners
Learner-centered approach
Learning principles – Context, Overviews, Chunking, Spacing
Feedback
Behavioral self-management
SMART goal-setting
Notes: Complete Narration: “Here are some key training-related terms and concepts we have covered. Can you define or explain each? Key concepts have included classroom training, web-based training, learning goals and objectives, KSAs, characteristics of adult learners, the learner-centered approach, learning principles (such as context, overviews, chunking, and spacing), feedback, behavioral self-management, and “SMART” goal-setting.
_______________
Additional instructor Note: You should be prepared to ask the class one or two review or discussion questions on each of these items. Example: Q: In regard to SMART goal-setting, can you remember what any 3 of the 5 letters in “SMART” stand for? A: S, Specific behaviors targeted; M, Motivationally effective; A, Attainable, R, Relevant, and T, Trackable.”

## Slide 226: Stages of Behavior Change
Contemplation
Pre-
Contemplation
Action
Preparation
Maintenance
Health, Wellness, Alertness, Performance
Notes: Complete Narration: “Finally, let’s walk up the steps or stages of behavior change. In behavior change, one progresses through five stages: pre-contemplation, contemplation, preparation, action, and maintenance. The prize? Health, wellness, alertness, and high performance!”
______________
Additional instructor note: This slide concludes the program by reviewing the stages and re-emphasizing that the trainer role is to facilitate behavior change by imparting knowledge, skills, and attitudes supportive of better sleep and fatigue management.

## Slide 227: Course Exam: Module 5
Instructions
30 Questions (both training & fatigue-related)